## Slide 1: ELEC2041 Microprocessors and Interfacing Lecture 11: Memory Access - I http://webct.edtec.unsw.edu.au/
March 2005
Saeid Nooshabadi
saeid@unsw.edu.au

## Slide 2: Overview
Memory Access in Assembly
Data Structures in Assembly
Notes: credential:
bring a computer
die photo
wafer
:
This can be an hidden slide. I just want to use this to do my own planning.
I have rearranged Culler’s lecture slides slightly and add more slides. This covers everything he covers in his first lecture (and more) but may
We will save the fun part, “ Levels of Organization,” at the end (so student can stay awake): I will show the internal stricture of the SS10/20.
Notes to Patterson: You may want to edit the slides in your section or add extra slides to taylor your needs.

## Slide 3: Review:Instruction Set (ARM 7TDMI)
Set of instruction that a processor can execute
Instruction Categories
  Data Processing or Computational (Logical and Arithmetic
  Load/Store (Memory Access: or transferring data between memory and registers)
  Control Flow (Jump and Branch)
  Floating Point
    coprocessor
  Memory Management
  Special
Registers

## Slide 4: Review: ARM Instructions So far
  add, sub, mov
  and, bic, orr, eor
  Data Processing Instructions with shift and rotate
  lsl, lsr, asr, ror
  Multiplications
  mul, mla, umull, umlal, smull,
  smlal

## Slide 5: Assembly Operands: Memory
C variables map onto registers; what about large data structures like arrays?
1 of 5 components of a computer: memory contains such data structures
But ARM arithmetic instructions only operate on registers, never directly on memory.
Data transfer instructions transfer data between registers and memory:
  Memory to register
  Register to memory

## Slide 6: Data Transfer: Memory to Reg (#1/4)
To transfer a word of data, we need to specify two things:
  Register: specify this by number (r0 – r15)
  Memory address: more difficult
    Think of memory as a single one-dimensional array, so we can address it simply by supplying a pointer to a memory address.
    Other times, we want to be able to offset from this pointer.
arr[0]
arr[1]
arr[2]
arr[3]
arr[4]

## Slide 7: Data Transfer: Memory to Reg (#2/4)
To specify a memory address to copy from, specify two things:
  A register which contains a pointer to memory
  A numerical offset (in bytes), or a register which contain an offset
The desired memory address is the sum of these two values.
Example: [v1, #8]
  specifies the memory address pointed to by the value in v1, plus 8 bytes
Example: [v1, v2]
  specifies the memory address pointed to by the value in v1, plus v2

## Slide 8: Data Transfer: Memory to Reg (#3/4)
Load Instruction Syntax:
  1 2, [3, 4]
  where
  1) operation name
  2) register that will receive value
  3) register containing pointer to memory
  4) numerical offset in bytes, or another shifted index register
Instruction Name:
  ldr (meaning Load register, so 32 bits or one word are loaded at a time from memory to register)

## Slide 9: Data Transfer: Memory to Reg (#4/4)
Example: ldr a1, [v1, #8]
  This instruction will take the pointer in v1, add 8 bytes to it, and then load the value from the memory pointed to by this calculated sum into register a1
Notes:
  v1 is called the base register
  8 is called the offset
  offset is generally used in accessing elements of array: base reg points to beginning of array
Example: ldr a1, [v1, v2]
  This instruction will take the pointer in v1, add an index offset in register v2 to it, and then load the value from the memory pointed to by this calculated sum into register a1
Notes:
  v1 is called the base register
  v2 is called the index register
  index is generally used in accessing elements of array using an variable index: base reg points to beginning of array
arr[0]
arr[1]
arr[2]
arr[3]
25
#8

## Slide 10: Data Transfer: Other Mem to Reg Variants (#1/2)
Pre Indexed Load Example:
ldr a1, [v1,#12]!
  This instruction will take the pointer in v1, add 12 bytes to it, and then load the value from the memory pointed to by this calculated sum into register a1.
  Subsequently, v1 is updates by computed sum of v1 and 12, ( v1  v1 + 12).
Pre Indexed Load Example:
ldr a1, [v1, v2]!
  This instruction will take the pointer in v1, add an index offset in register v2 to it, and then load the value from the memory pointed to by this calculated sum into register a1.
  Subsequently, v1 is updated by computed sum of v1 and v2, (v1 v1 + v2).

## Slide 11: Data Transfer: Other Mem to Reg Variants (#2/2)
Post Indexed Load Example:
ldr a1, [v1], #12
  This instruction will load the value from the memory pointed to by value in register v1 into register a1.
  Subsequently, v1 is updates by computed sum of v1 and 12, ( v1  v1 + 12).
Example: ldr a1, [v1], v2
  This instruction will load the value from the memory pointed by value in register v1, into register a1.
  Subsequently, v1 is updated by computed sum of v1 and v2, ( v1  v1 + v2).

## Slide 12: Data Transfer: Reg to Memory (1/2)
Also want to store value from a register into memory
Store instruction syntax is identical to Load instruction syntax
Instruction Name:
str (meaning Store from Register, so 32 bits or one word are stored from register to memory at a time)

## Slide 13: Data Transfer: Reg to Memory (2/2)
Example: str a1,[v1, #12]
  This instruction will take the pointer in v1, add 12 bytes to it, and then store the value from register a1 into the memory address pointed to by the calculated sum
Example: str a1,[v1, v2]
  This instruction will take the pointer in v1, adds register v2 to it, and then store the value from register a1 into the memory address pointed to by the calculated sum.

## Slide 14: Data Transfer: Other Reg to Mem Variants (#1/2)
Pre Indexed Store Example:
str a1, [v1,#12]!
  This instruction will take the pointer in v1, add 12 bytes to it, and then store the value from register a1 into the memory address pointed to by the calculated sum.
  Subsequently, v1 is updates by computed sum of v1 and 12, ( v1  v1 + 12).
Pre Indexed Store Example:
str a1,[v1, v2]!
  This instruction will take the pointer in v1, adds register v2 to it, and then store the value from register a1 into the memory address pointed to by the calculated sum.
  Subsequently, v1 is updated by computed sum of v1 and v2 ( v1  v1 + v2).

## Slide 15: Data Transfer: Other Reg to Mem Variants (#2/2)
Post Indexed Store Example:
str a1, [v1],#12
  This instruction will store the value from register a1 into the memory address pointed to by register v1.
  Subsequently, v1 is updates by computed sum of v1 and 12, ( v1  v1 + 12).
Post Indexed Store Example:
str a1,[v1], v2
  This instruction will store the value from register a1 into the memory address pointed to by register v1.
  Subsequently, v1 is updated by computed sum of v1 and v2, ( v1  v1 + v2).

## Slide 16: Pointers v. Values
Key Concept: A register can hold any 32-bit value. That value can be a (signed) int, an unsigned int, a pointer (memory address), etc.
If you write add v3,v2,v1 then v1 and v2 better contain values
If you write ldr a1,[v1] then v1 better contain a pointer
Don’t mix these up!

## Slide 17: Addressing: Byte vs. halfword vs. word
Every word in memory has an address, similar to an index in an array
Early computers numbered words like C numbers elements of an array:
  Memory[0], Memory[1], Memory[2], …
Computers needed to access 8-bit bytes, half words (2 bytes/halfword) as well as words (4 bytes/word)
Today machines address memory as bytes, hence
  Half word addresses differ by 2
  Memory[0], Memory[2], Memory[4], …
  word addresses differ by 4
  Memory[0], Memory[4], Memory[8], …
Called the “address” of a word

## Slide 18: Compilation with Memory
What offset in ldr to select my_Array[8] in C?
4x8=32 to select my_Array[8]: byte v. word
Compile by hand using registers: g = h + my_Array[8];
  g: v1, h: v2, v3: base address of my_Array
1st transfer from memory to register:
ldr v1, [v3,#32] ; v1 gets my_Array[8]
  Add 32 to v3 to select my_Array[8], put into v1
Next add it to h and place in g add v1,v2,v1 ; v1 = h+ my_Array[8]

## Slide 19: Same thing in pictures
v1
v2
v3
g
h
my_Array[0]
0
0xFFFFFFFF
my_Array[8]
my_Array
ldr v1, [v3,#32]
  Adds offset “8 x 4 = 32” to select my_Array[8], and puts into a1
The value in register v3 is an address
Think of it as a pointer into memory
v3 contains the address of the Base of the my_Array .
add v1, v2,v1
  The value in register v1 is the sum of v2 and v1.
v1 + v2
32

## Slide 20: Compile with variable index
What if array index not a constant? g = h + my_Array[i];
  g: v1, h: v2, i: v3, v4: base address of my_Array
To load my_Array[i] into a register, first turn i into a byte address; multiply by 4
How multiply using adds?
  i + i = 2i, 2i + 2i = 4i
mov a1,v3 ; a1 = i
add a1,a1,a1 ; a1 = 2*i
add a1,a1,a1 ; a1 = 4*i
Better alternative: mov a1, v3, lsl #2

## Slide 21: Compile with variable index, con’t
Now load my_Array[i]= my_Array[0 + 4*i] into v1 register:
ldr v1, [v4, a1] ;v1= my_Array[i]
Finally add to h to it and put sum in g:
add v1,v1, v2 ;g = h + my_Array[i]

## Slide 22: Compile with variable index: Summary
C statement:
g = h + my_Array[i];
Compiled ARM assembly instructions:
mov a1, v3, lsl #2 ; a1 = 4*i
ldr v1, [v4, a1] ;v1= my_Array[i]
Finally add to h to it and put sum in g:
add v1,v1, v2 ;g = h + my_Array[i]
Base Reg Index Reg

## Slide 23: Compile with variable index Example
Compile this into ARM code:
B_Array[i] = h + A_Array[i];
  h: v1, i:v2, v3:base address of A_Array, v4:base address of B_Array

## Slide 24: Compile with variable index Example (Solution)
Compile this C code into ARM:
B_Array[i] = h + A_Array[i];
  h: v1, i:v2, v3:base address of A_Array, v4:base address of B_Array
mov a1, v2, lsl #2 ;a1 = 4*i
ldr a2, [v3, a1] ; v3 + a1 = ;addrA_Array[i] ;a2= A_array[i]
add a2, a2, v1 ;a2 = h + A_Array[i];
str a2, [v4, a1] ; v4 + a1 = ;addrB_Array[i] ;B_Array[i]= a2
Base Reg Index Reg

## Slide 25: ELEC2041 Reading Materials (Week #4)
Week #4: Steve Furber: ARM System On-Chip; 2nd Ed, Addison-Wesley, 2000, ISBN: 0-201-67519-6. We use chapters 3 and 5
ARM Architecture Reference Manual –On CD ROM

## Slide 26: Computers in the News
Motorola i.MX21 Applications Processor
For robust multimedia applications, with higher levels of video and graphics capabilities, plug and play connectivity, and added security features.
  Starting at 266 MHz processor performance using ARM926EJ-S with Jazelle Java acceleration
  Enhanced video support with real-time MPEG4 and H.263 encoding and decoding with pre- and post-processing
  3D graphics support through external bus master interface to reduce overhead
  Enhanced security including high assurance boot, security controller, hash accelerator, and memory management
  Connectivity with 4x UARTs, IrDA, USB-On-the-Go, and to 2.5G cellular platforms through i.Smart reference design
http://motorola.com/imx

## Slide 27: Notes about Memory
Pitfall: Forgetting that sequential word addresses in machines with byte addressing do not differ by 1.
  Many an assembly language programmer has toiled over errors made by assuming that the address of the next word can be found by incrementing the address in a register by 1 instead of by the word size in bytes.
  So remember that for both ldr and str, the sum of the base address and the offset must be a multiple of 4 (to be word aligned)

## Slide 28: More Notes about Memory: Alignment (#1/2)
3 2 1 0
Aligned
Not
Aligned
ARM requires that all words start at addresses that are multiples of 4 bytes
Called Alignment: objects must fall on address that is multiple of their size.
Some machines like Intel allow non-aligned accesses

## Slide 29: More Notes about Memory: Alignment (#2/2)
Non-Aligned memory access causes byte rotation in right direction within the word
0 1 2 3
0x80
09 82 a2 2e
0x83 0x82 0x81 0x80
ldr a1, 0x80 a1 = 0x0982a22e
ldr a1, 0x81 a1 = 0x2e0982a2
ldr a1, 0x82 a1 = 0xa22e0982
ldr a1, 0x83 a1 = 0x82a22e09

## Slide 30: Role of Registers vs. Memory
What if more variables than registers?
  Compiler tries to keep most frequently used variable in registers
  Writing less common to memory: spilling
Why not keep all variables in memory?
  Smaller is faster: registers are faster than memory
  Registers more versatile:
    ARM Data Processing instructions can read 2, operate on them, and write 1 per instruction
    ARM data transfer only read or write 1 operand per instruction, and no operation

## Slide 31: “And in Conclusion…” (#1/2)
In ARM Assembly Language:
  Registers replace C variables
  One Instruction (simple operation) per line
  Simpler is Better
  Smaller is Faster
Memory is byte-addressable, but ldr and str access one word at a time.
A pointer (used by ldr and str) is just a memory address, so we can add to it or subtract from it (using offset).
Word Addresses n Memory should be word aligned

## Slide 32: “And in Conclusion…”(#2/2)
New Instructions:
  ldr, str