APPLICATIONS AND USES OF PALM AND PALM KERNEL OILS IN SPECIALITY PRODUCTS

E. M. Goh

Lam Soon (M) Berhad

[Presented at the MOSTA Short Course 8, April 8-9, 2002, Genting Highlands, Malaysia]

Introduction

Speciality fats are mainly confectionery fats of the following types:

- Cocoa Butter Equivalent (CBE)

- Cocoa Butter Substitute (CBS)

- Toffee Fat

- Non-Dairy Fat

- Cream Filling Fat

- General Purpose Coating Fat

Palm oil and palm kernel oil are ideal raw materials for the production of speciality fats. Palm oil contains about 50% of the long-chain saturated fatty acids of which palmitic acid constitutes about 44% (Table 1). Palm oil also contains a significant amount of the symmetrical SOS-type triglyceride which is one of the major triglycerides present in cocoa butter (Table 2). Palm kernel oil and coconut oil are the two lauric oils which are of commercial importance. These two oils are interchangeable in many applications because of their similarities in properties. However, palm kernel oil contains a higher amount of oleic acid than coconut oil (Table 3). This makes palm kernel oil a very suitable oil for hydrogenation (hardening) for the production of speciality fats with different end-use melting points and hardness. Palm and palm kernel oils, like most of other vegetable oils in their original state, have a limited application when utilised as such. Hence their properties have to be modified in order to extend the range of utilisation.

Base Oil Modification Processes

The following processes are commonly used for the production of speciality fats:

- Fractionation,

- Hydrogenation, and

- Interesterification

Fractionation

Fractionation is a process by which an oil is separated into liquid and solid fractions. The three fractionation processes used commercially are:

- Dry fractionation,

- Detergent fractionation, and

- Solvent  fractionation

Hydrogenation

Hydrogenation is carried out to remove the unsaturation of fatty acids and hence to increase the oxidative stability and melting point of oils. Depending on the extent of hydrogenation, the oils and fats can be modified to products of various hardnesses, thus giving a wider range of utilisation.

Table 1. Typical Fatty Acid Compositions (%)

| Fatty Acids | Cocoa Butter | Palm Oil | Beef Tallow |
| --- | --- | --- | --- |
| 14:0 16:0 18:0 18:1 18:2 18:3 | 26.5 35 35 3 | 1 44 4.5 39 10 0.5 | 3 26 19.5 40 3.5 0.5 |
| Total Saturated | 61.5 | 49.5 | 48.5 |

Table 2. Typical Triglyceride Compositions (%)

| Triglyceride | CocoaButter | Palm Oil | Palm Olein | Beef Tallow |
| --- | --- | --- | --- | --- |
| SSS S2U of which : SOS SSU SPS SU2 UUU | 3 82 75 0.5 6.5 14 1 | 8 48 33 6 9 37 7 | < 1 49.5 34.5 6.5 9 41 9 | 8 39 25 11 3 41 12 |

S = Total Saturated Acids, U = Total Unsaturated Acids,

O = Monounsaturated Acids, P = Polyunsaturated Acids

### Table 3. Fatty Acid Composition of Coconut Oil and

### Palm Kernel Oil

| Coconut Oil | Fatty Acids | Palm kernel Oil |
| --- | --- | --- |
| 15% 48 18 9 2 6 3 | Short Chain Saturated Acids Lauric Acid (12:0) Myristic Acid (14:0) Palmitic Acid (16:0) Stearic Acid (18:0) Oleic Acid (18:1) Linoleic Acid (18:2) | 8% 48 16 8 2 15 3 |

Controlled hydrogenation of palm kernel oil with a melting point of about 27-28°C produces a useful range of hydrogenated (hardened) palm kernel fats with melting points of 32-41°C (Fig. 1).

Interesterification

Interesterification (or rearrangement) is a process which alters the distribution of fatty acids in the glycerol moiety of triglyceride, thus producing fats with different melting and crystallisation characteristics compared to the uninteresterified fat.

The effect of interesterification on the triglyceride composition of a mixture of palm and palm kernel oils with different chemical compositions is clearly shown in Fig. 2.

Classification and Production of Speciality Fats

Speciality fats can be classified according to their chemical compositions into three types, namely:

Symmetrical,

Lauric, and

High-trans

Symmetrical-type speciality fats contain predominantly symmetrical SOS-type triglycerides. The major triglycerides POSt, StOSt and POP in cocoa butter are often summarised as SOS triglycerides.

Solvent fractionation of palm oil (Fig. 3) produces a mid-fraction with a high content of the POP triglyceride.1 By blending this palm mid-fraction with Illipe fat which contains StOSt and POSt triglycerides a Cocoa Butter Equivalent (CBE) fat with physico-chemical characteristics similar to those of cocoa butter can be produced.2

Lauric-type speciality fats are produced from oils containing mainly of triglycerides of lauric and myristic acids. For instance, hydrogenation of palm kernel oil produces a range of lauric-type fats with slip melting points varying from 32 to 41°C. Palm kernel oil can also be fractionated by dry, detergent or solvent fractionation to give a stearin with much better melting properties than the hydrogenated palm kernel fats. The palm kernel stearin with physical properties such as the high solid fat contents and steep melting profile resembling cocoa butter is usually described as Cocoa Butter Substitute (CBS). A typical melting curve of hydrogenated palm kernel stearin is shown in Fig. 4.

High-trans-type fats can be produced by selectively hydrogenating palm olein, or by a combination of selective hydrogenation and fractionation from liquid oils such as soyabean oil or blends of oils.3 These fats are easily distinguished from cocoa butter by their content of trans acids (Table 4). The melting properties of some high-trans-type speciality fats are given in Table 5. They are sometimes called cocoa butter partial replacers because they are more compatible with cocoa butter than the lauric-type CBS.

Table 4. Comparison of Fatty Acid Compositions

#### (%)  of Cocoa Butter and A High-Trans-

#### Type Speciality Fat

| Acid | Cocoa Butter | High-Trans Fat |
| --- | --- | --- |
| 16 : 0 18 : 0 18 : 1 cis 18 : 1 trans | 26 32 34 0 | 23 12 16 46 |

Table 5. Melting Properties of Some High-Trans-

Type Speciality Fats

| Speciality Fat | Solid Fat Content |
| --- | --- |
|  | 200C | 250C | 300C | 350C | 400C |
| Biscuitine CT Cessanova Kaomel Kemfat 550 CBR (LS) Cocoa butter | 74 76 75 75 74 80 | 62 62 65 64 58 76 | 40 43 54 44 38 50 | 19 18 20 22 17 0 | 0 3 0 3 0 |

Applications of Speciality Fats

Non-Dairy Products

Unhydrogenated (or unhardened) palm kernel oil and olein are ideal fats for the manufacture of non-dairy products. They can be used as fast-setting chocolate coating fats for ice cream and other deep-frozen confections. The coatings set quickly when applied on to ice cream. These palm kernel fats are more suitable and perform better than cocoa butter for this purpose because the coatings formed are hard but not brittle whereas pure chocolate coating (with cocoa butter) sets too hard, is brittle and flakes off easily. A typical ice cream coating formulation is given in Table 6.

#### Table 6. A Typical Ice Cream Coating Recipe

| Ingredient | % |
| --- | --- |
| Cocoa powder (10 - 12%) Icing (fine) sugar Fat Lecithin | 14 25.5 60 0.5 |

Coatings and Filler Creams

The hydrogenated lauric fats with melting points of 32-41°C can be used as coating fats. These lauric fats have high solids at room temperature and melt rapidly enough to produce fairly good quality coating systems. Hydrogenated palm kernel oil with melting point of 39-41°C is used for coating wafers. However, those with high melting points melt above body temperature and therefore produce a waxy mouthfeel. Coatings made from hydrogenated palm kernel oil and interesterified palm kernel oil have moderate resistance to fat bloom and the gloss is inferior to those based on fractionated palm kernel stearin. Palm kernel fats interesterified with/without a small amount of palm oil can also be used for the preparation of cheap and intermediate grade coatings with firm but not very brittle texture at ambient temperature and good melting properties. Hydrogenated palm kernel olein can be used in the formulation of bakery coatings and glazes for cakes and biscuit creams. Cream filling between wafers requires fats which set quickly and yet melt cleanly in the mouth giving a cool sensation on the palate. Hydrogenated palm kernel oleins are ideal for this formulation.

Toffees

Hydrogenated palm kernel oil or olein is largely used as a cheaper alternative toffee fat to replace the more expensive dairy butter, either completely or to combine with butter in the making of toffees. The physical characteristics of some of these fats are shown in Table 7. The inclusion of these fats in toffees retains the good texture by giving body to the products and offering resistance to moisture penetration. They also provide lubrication and chewiness to the products. Typical recipes for toffees are given in Table 8.

Coffee Whiteners

Since coffee whiteners are used at higher temperatures, they can be formulated based on hydrogenated palm kernel oil or olein with melting points of 35-42°C and high solid contents at room temperature. These hydrogenated fats have very low or no unsaturation and therefore are more resistant to the development of off-flavours due to oxidation. A typical coffee whitener formulation is given in Table 9.

Whipped Toppings

These products are regularly formulated using hydrogenated palm kernel oil, hydrogenated palm kernel stearin, or blends of the two (for economy) which impart an easy air incorporation during whipping and give high solids content required for foam stiffness.

Substitute Chocolates/Compound Coatings

Palm kernel stearin based CBS is suitable for the manufacture of solid or hollow-molded products with excellent mold release, good snap, steep melting characteristics and good flavour release and resistance to fat bloom. Although substitute chocolate formulated from lauric fats forms stable crystals on rapid cooling without tempering which simplifies production plant and reduces costs, palm kernel stearin based CBS forms eutectic mixtures with cocoa butter, i.e. the fat is not compatible with cocoa butter. It can only tolerate a limited, small, amount of cocoa butter,4,5 and therefore must substitute for all the cocoa butter in the recipe if a good chocolate is to be made. Hence in substitute chocolate or other coating formulations, the CBS based coating must be formulated with low-fat cocoa powder in order to avoid incompatibility with cocoa butter. Coatings formulated with these fractionated lauric fats are very similar to real chocolate (made using cocoa butter) in set-up, shrink, snap and eating qualities. A typical substitute chocolate made with CBS is shown in Table 10.

CBE fat which is compatible with cocoa butter in almost any proportions, can be used in “chocolate”/coatings. In certain countries where legislations allow, even up to about 15% of the cocoa butter in chocolate may be replaced by a CBE fat and the product may still be described as “chocolate”. In

Table 7. Physical Characteristics of Toffee Fats

|  | HPKO | HPKO | HPKOL | HPKOL | Butter Fat |
| --- | --- | --- | --- | --- | --- |
| Melting point (0C) Solid Fat Content (% by NMR) at 200C 250C 300C 350C 400C | 37 64 39 14 7 2 | 41 77 58 31 15 7 | 37 63 37 12 4 0 | 41 73 53 28 14 6 | 34 22 13 7 4 0 |

HPKO = Hydrogenated Palm Kernel Oil, HPKOL = Hydrogenated Palm Kernel Olein

# Table 8. Recipes for The Manufacture of Toffee

| “European” Recipe | Ingredient | “Tropical” Recipe |
| --- | --- | --- |
| 23 34 28 11 4 | Granulated sugar Glucose syrup Skimmed sweetened condensed milk Vegetable fat Water | 15 43 28 11 3 |
| 100 parts 0.4 | salt | 100 parts 0.4 |

#### Table 9. A Typical Powder Coffee Whitener

#### Recipe6

| Ingredient | % |
| --- | --- |
| Corn syrup solid Fat* Sodium caseinate Emulsifier Phosphate salt | 55 - 60 35 - 40 4.5 - 5.5 0.2 - 0.5 1.2 - 1.8 |

* Hardened palm kernel oil or olein SMP ~ 40oC

terms of texture and flavour these products are very close to real (cocoa butter) chocolate. Typical formulations using CBEs are given in Table 11.

#### Table 10. A Typical Substitute Chocolate Recipe

| Ingredients |  |
| --- | --- |
| Cocoa powder Icing sugar Skimmed milk powder ChocoAce Premier (CBS) | 8 44 20 28 |
| + Lecithin + Vanillin | 100 parts 0.4 0.1 |

#### Table 11. A Typical Formulation Using CBEs7

|  | Dark Chocolate | Dark Coating | Milk Chocolate | Milk Coating |
| --- | --- | --- | --- | --- |
| Cocoa mass Sugar Full cream Milk powder Cocoa butter CBE | 40 45 - 10 5 | 40 45 - - 15 | 10 45 25 15 5 | 10 45 25 - 20 |
|  | 100% | 100% | 100% | 100% |

CBE = Cocoa Butter Equivalent

Table 12. Oxidative Stability Determined by

#### Rancimat

|  | Time in hours at 120oC |
| --- | --- |
| Soyabean oil Palm kernel oil Hardened palm kernel olein (MP = 350C) Hardened palm kernel oil (MP = 400C) Hardened palm kernel stearin | 4 11 16 41 42 |

Stability of Speciality Fats

Speciality fats produced from palm and palm kernel oils, especially the hydrogenated fats, are very stable against oxidation. The oxidative stability of some palm kernel products, determined by a Rancimat apparatus, is shown in Table 12. The only serious disadvantage of using palm kernel and other lauric fats is that in the presence of moisture and enzyme lipase, hydrolytic fat splitting can occur, liberating the short-chain fatty acids (C6:0 to C12:0) which may give rise to unpleasant soapy off-flavour. In view of this sensitivity of lauric fats to hydrolysis good manufacturing practices, such as using fresh and good quality raw materials and precautions to prevent post- infection, are needed when using lauric fats in food products.

Conclusion

The unique properties of palm and palm kernel oils have made these two oils particularly attractive to the confectionery industry. Palm and palm kernel oils, with modification, are undoubtedly ideal raw materials for the production of various speciality fats which include CBE, CBS, toffee fats, non-dairy fats and cream filling fats. These fats are used in products such as chocolates/coatings, toffees, coffee whiteners, whipped toppings, filler creams and non-dairy products.

Although palm kernel and coconut oils are interchangeable in application it appears that the utilisation of palm kernel based confectionery fats is increasing at the expense of coconut based fats. With continuous increase in production of palm and palm kernel oils these two oils are expected to remain available in quantities sufficient to meet the demands by speciality fat users.

References

- Torrey S (1983). “Edible Oils and Fats – Developments Since 1978”, Noyes Data Corporation, Park Ridge, New Jersey, U.S.A.

- Wolfe JA (1977). “C.B.E.’s and Codex”, The Manufacturing Confectioner, April, 53.

- Paulicka FR (1981). “Non-Lauric Substitute and Replacer Confectionery Coating Fats”, Candy & Snack Industry, 146, 46.

- Paulicka FR (1973). “Phase Behaviour of Cocoa Butter Extenders”, Chem. Ind. (London), 1st September, 835.

- Gordon MH, FB Padley and RE Timms (1979). “Factors Influencing the Use of Vegetable Fats in Chocolate”, Fette Seifen Anstrichm. 81, 116.

- Weiss TJ (1983). “Food Oils and Their Uses”, Ellis Horwood Ltd., Chichester, England, 2nd edition.

- Durkee Industrial Foods (1982). “Specialist Fats for Chocolate and Coatings”, Confectionery Production, November, 450.

# Text boxes

# Figure 1. Solid Fat Contents of Palm Kernel Oil at

##### Different Degrees of Hydrogenation

Figure 3. Acetone Fractionation of Palm Oil

# Figure 2. Interesterification of A Mixture of Palm

# and Palm Kernel Oils (50/50)

# Figure 4. Solid Fat Contents of Hardened PK

# Stearin,Cocoa Butter and Hardened PK Oil