Digitech ValveFX

Program Dump SysEx Format

Brian Shrader

October 1998

This documents was originally the Digitech RP10/RP12 Program Dump SysEx Format document written by:

Bruce James

bjames@clear.net.nz  or  bjames@voyager.co.nz

April 1997

Which was derived in part from the GSP-2101 Module/Parameter Data document by Tom Owens (exigy@one.net) and the S-DISC System Exclusive Documentation.  The remainder from hours James spent pushing buttons on the RP-10 and studying sysex dumps, and hours I spent pushing buttons on the ValveFX and studying sysex dumps.

# SysEx Format

For a program patch dump.

| Description | Hex Value(s) | Size (bytes) | Offset |
| --- | --- | --- | --- |
| SysEx “Begin Message” | F0 | 1 | 0 |
| Manufacturer’s ID = “Digitech” | 00 00 10 | 3 | 1 |
| Channel Number - 1 (nn= 01 to 0F) | nn 00 = channel 1 01 = channel 2 … | 1 | 4 |
| Device Number = “ValveFX” | 45 | 1 | 5 |
| Procedure Number = “Receive One Program” | 42 | 1 | 6 |
| Program Number (-1) | hh ll 00 00 = program 1 | 2 | 7 |
| Algorithm Number (+40h-1) | hh ll 00 40 = algorithm 1 | 2 | 9 |
| Program Name ( n = 0 to 15 characters) | 00 cc … | s1 = n * 2, 30 (max) | 11 |
| Carriage Return | 00 0D | 2 | s1+11 |
| Algorithm Name (n = 0 to 16 characters) | 00 cc … | s2 = n * 2, 32 (max) | s1+13 |
| NULL (ends character strings) | 00 00 | 2 | s1+s2+13 |
| Number of Linked Local CC’s (nn = 00 to 0A) | 00 nn | 2 | s1+s2+15 |
| Linked Local CC Values (n = 0 to 10 CC’s) | see Linked Local CC format below | s3 = n * 14, 140 (max) | s1+s2+17 |
| Number of Parameters | hh ll | 2 | s1+s2+s3+15 |
| Parameter Values | see Algorithm Module format below | s4 | s1+s2+s3+17 |
| Z-Reg init count | hh ll | 2 | s1+s2+s3+s4+15 |
| Z-Reg init strings | cc … | s5 | s1+s2+s3+s4+17 |
| SysEx “End Message” | F7 | 1 | s1+s2+s3+s4+s5+17 |
|  |  |  | s1+s2+s3+s4+s5+17 |

# Linked Local CC Format

For each Linked Local CC

| Parameters | Size (bytes) | Offset |
| --- | --- | --- |
| Link# | 2 | 0 |
| CC# | 2 | 2 |
| Parameter# | 2 | 4 |
| Maximum Value | 4 | 6 |
| Minimum Value | 4 | 10 |
|  |  | 14 |

# Algorithm Module Format

### Common

(Starts all algorithms)

| Module |  | Size (bytes) | Offset |
| --- | --- | --- | --- |
| Compressor | Comp | 6 | 0 |
| Distortion | Dist | 10 | 6 |
| Noise Gate | NGt | 14 | 16 |
| Master Level | MLvl | 2 | 30 |
| 4 Band Parametric Equalizer | PEQ | 24 | 32 |
| Cabinet Emulator | CabEm | 4 | 56 |
| Mixers | Mixers | 2 | 58 |
| Master Mix | MMIX | 2 | 60 |
|  |  |  | 64 |

### Algorithm #1  DCho -> 2TDly -> Revrb

| Module |  | Size (bytes) | Offset |
| --- | --- | --- | --- |
| Dual Chorus | DCho | 14 | 64 |
| 3x3 Mixer | 3x3 | 12 | 78 |
| 2 Tap Delay 0.8 Sec | 2TDly | 16 | 94 |
| 4x3 Mixer | 4x3 | 16 | 110 |
| Multi-FX Reverb | MVerb | 18 | 128 |
| 4x2 Mixer | 4x2 | 18 | 146 |
|  |  |  | 164 |

### Algorithm #2  DDtn -> 2TDly -> Revrb

| Module |  | Size (bytes) | Offset |
| --- | --- | --- | --- |
| Dual Detune | DDtn | 10 | 64 |
| 3x3 Mixer | 3x3 | 12 | 74 |
| 2 Tap Delay 0.8 Sec | 2TDly | 16 | 90 |
| 4x3 Mixer | 4x3 | 16 | 106 |
| Multi-FX Reverb | MVerb | 18 | 124 |
| 4x2 Mixer | 4x2 | 18 | 142 |
|  |  |  | 160 |

### Algorithm #3  DFla -> 2TDly -> Revrb

| Module |  | Size (bytes) | Offset |
| --- | --- | --- | --- |
| Dual Flanger | DFla | 14 | 64 |
| 3x3 Mixer | 3x3 | 12 | 78 |
| 2 Tap Delay 0.8 Sec | 2TDly | 16 | 94 |
| 4x3 Mixer | 4x3 | 16 | 110 |
| Multi-FX Reverb | MVerb | 18 | 128 |
| 4x2 Mixer | 4x2 | 18 | 146 |
|  |  |  | 164 |

### Algorithm #4  DPha -> 2TDly -> Revrb

| Module |  | Size (bytes) | Offset |
| --- | --- | --- | --- |
| Mono Tremolo | Trm | 8 | 64 |
| Dual Phaser | DPha | 12 | 72 |
| 3x3 Mixer | 3x3 | 12 | 84 |
| 2 Tap Delay 0.8 Sec | 2TDly | 16 | 100 |
| 4x3 Mixer | 4x3 | 16 | 116 |
| Multi-FX Reverb | MVerb | 18 | 134 |
| 4x2 Mixer | 4x2 | 18 | 152 |
|  |  |  | 170 |

### Algorithm #5  Pch -> 2TDly -> Revrb

| Module |  | Size (bytes) | Offset |
| --- | --- | --- | --- |
| Pitch Shifter | Pch | 12 | 64 |
| 2x1 Mixer | 2x1 | 4 | 76 |
| 2 Tap Delay 0.8 Sec | 2TDly | 16 | 80 |
| 3x1 Mixer | 3x1 | 6 | 96 |
| Multi-FX Reverb | MVerb | 18 | 102 |
| 3x2 Mixer | 3x2 | 12 | 120 |
|  |  |  | 132 |

### Algorithm #6  DCho -> 2TDly -> 2 Pans

| Module |  | Size (bytes) | Offset |
| --- | --- | --- | --- |
| Dual Chorus | DCho | 14 | 64 |
| 3x1 Mixer | 3x1 | 6 | 78 |
| 2 Tap Delay 1.4 Sec | 2TDly | 16 | 84 |
| 5x2 Mixer | 5x2 | 20 | 100 |
| Auto Panner A | Pan | 8 | 120 |
| Auto Panner B | Pan | 8 | 128 |
| 7x2 Mixer | 7x2 | 28 | 136 |
|  |  |  | 164 |

### Algorithm #7  Cho -> Pch -> 4TDly

| Module |  | Size (bytes) | Offset |
| --- | --- | --- | --- |
| Mono Chorus | Cho | 12 | 64 |
| 2x1 Mixer | 2x1 | 4 | 76 |
| Pitch Shifter | Pch | 12 | 80 |
| 2x1 Mixer | 2x1 | 4 | 92 |
| 4 Tap Delay 1.4 Sec | 4TDly | 24 | 96 |
| 5x2Mixer | 5x2 | 20 | 120 |
|  |  |  | 140 |

### Algorithm #8  Dly -> Revrb -> SDuc

| Module |  | Size (bytes) | Offset |
| --- | --- | --- | --- |
| Mono Delay 1.0 Sec | Dly | 12 | 64 |
| 2x1 Mixer | 2x1 | 4 | 76 |
| Multi-FX Reverb | MVerb | 18 | 80 |
| Stereo Ducker | SDuc | 12 | 98 |
| 3x2 Mixer | 3x2 | 12 | 110 |
|  |  |  | 122 |

### Algorithm #9  DCho -> 2TDly/STrem

| Module |  | Size (bytes) | Offset |
| --- | --- | --- | --- |
| Dual Chorus | DCho | 14 | 64 |
| 3x2 Mixer | 3x2 | 12 | 78 |
| 2 Tap Delay 1.4 Sec | 2TDly | 16 | 90 |
| Stereo Tremolo | STrm | 8 | 106 |
| 5x2 Mixer | 5x2 | 20 | 114 |
|  |  |  | 134 |

### Algorithm #10  Wah -> Wham -> DCho -> SDly

| Module |  | Size (bytes) | Offset |
| --- | --- | --- | --- |
| Traditional Wah | Twah | 6 | 64 |
| Whammy | Wham | 6 | 70 |
| Dual Chorus | DCho | 14 | 86 |
| 3x2 Mixer | 3x2 | 12 | 90 |
| Stereo Delay 0.5 Sec | Sdly | 12 | 102 |
| 4x2 Mixer | 4x2 | 16 | 114 |
|  |  |  | 130 |

### Algorithm #11  Arpeggio2 -> 2Dly

| Module |  | Size (bytes) | Offset |
| --- | --- | --- | --- |
| Arpeggiator | Arp | 16 | 64 |
| Arpeggiator | Arp | 16 | 80 |
| 3x3 Mixer | 3x3 | 12 | 96 |
| 2 Tap Delay 0.4 Sec | 2TDly | 16 | 108 |
| 4x2 Mixer | 4x2 | 16 | 124 |
|  |  |  | 140 |

### Algorithm #12  Sampler -> GEQ10

| Module |  | Size (bytes) | Offset |
| --- | --- | --- | --- |
| Sampler 1.5 Sec | Smpl | 24 | 64 |
| 10 Band Graphic Equalizer | GEQ10 | 22 | 88 |
| Phase Inverter | Inv | 4 | 110 |
|  |  |  | 114 |

### Algorithm #13  2TDly -> 6VoiceCho

| Module |  | Size (bytes) | Offset |
| --- | --- | --- | --- |
| 2 Tap Delay 1.4 Sec | 2TDly | 16 | 64 |
| 3x2 Mixer | 3x2 | 12 | 80 |
| 4 Phase Chorus | 4PCho | 18 | 92 |
| Dual Chorus | DCho | 14 | 110 |
| 8x2 Mixer | 8x2 | 32 | 124 |
|  |  |  | 156 |

### Algorithm #14  Mod Dly -> Revrb

| Module |  | Size (bytes) | Offset |
| --- | --- | --- | --- |
| Modulated Delay 0.8 Sec | MDly | 16 | 64 |
| 2x3 Mixer | 2x3 | 8 | 80 |
| Multi-FX Reverb | MVerb | 18 | 88 |
| 4x2 Mixer | 4x2 | 18 | 106 |
|  |  |  | 124 |

### Algorithm #15  Wham -> 2TDly -> Revrb

| Module |  | Size (bytes) | Offset |
| --- | --- | --- | --- |
| Whammy | Wham | 6 | 64 |
| 2 Tap Delay 0.8 Sec | 2TDly | 16 | 70 |
| 3x1 Mixer | 3x1 | 6 | 86 |
| Multi-FX Reverb | MVerb | 18 | 92 |
| 5x2 Mixer | 5x2 | 20 | 110 |
|  |  |  | 130 |

### Algorithm #16  Wah -> BigVerb

| Module |  | Size (bytes) | Offset |
| --- | --- | --- | --- |
| Traditional Wah | Twah | 6 | 64 |
| BigVerb | Big | 28 | 70 |
| 3x2 Mixer | 3x2 | 12 | 98 |
|  |  |  | 110 |

### Algorithm #17  AWah -> Cho -> Dly

| Module |  | Size (bytes) | Offset |
| --- | --- | --- | --- |
| Automatic Wah | Awah | 6 | 64 |
| 4 Phase Chorus | 4PCho | 18 | 70 |
| 5x2 Mixer | 5x2 | 20 | 88 |
| Stereo Delay 0.5 Sec | SDly | 12 | 128 |
| 5x2 Mixer | 5x2 | 20 | 140 |
|  |  |  | 160 |

### Algorithm #18  DCho -> 4TDly -> Pan

| Module |  | Size (bytes) | Offset |
| --- | --- | --- | --- |
| Dual Chorus | DCho | 14 | 64 |
| 3x3 Mixer | 3x3 | 12 | 78 |
| 4 Tap Delay 1.4 Sec | 4TDly | 24 | 90 |
| 5x1 Mixer | 5x1 | 10 | 114 |
| 6x2 Mixer | 6x2 | 24 | 124 |
| Auto Panner | Pan | 8 | 148 |
| 4x2 Mixer | 4x2 | 16 | 156 |
|  |  |  | 172 |

### Algorithm #19  DDtn -> 4TDly -> Pan

| Module |  | Size (bytes) | Offset |
| --- | --- | --- | --- |
| Dual Detune | DDtn | 10 | 64 |
| 3x3 Mixer | 3x3 | 12 | 74 |
| 4 Tap Delay 1.4 Sec | 4TDly | 24 | 86 |
| 5x1 Mixer | 5x1 | 10 | 110 |
| 6x2 Mixer | 6x2 | 24 | 120 |
| Auto Panner | Pan | 8 | 144 |
| 4x2 Mixer | 4x2 | 16 | 152 |
|  |  |  | 168 |

### Algorithm #20  DFla -> 4TDly -> Pan

| Module |  | Size (bytes) | Offset |
| --- | --- | --- | --- |
| Dual Flange | DFla | 14 | 64 |
| 3x3 Mixer | 3x3 | 12 | 78 |
| 4 Tap Delay 1.4 Sec | 4TDly | 24 | 90 |
| 5x1 Mixer | 5x1 | 10 | 114 |
| 6x2 Mixer | 6x2 | 24 | 124 |
| Auto Panner | Pan | 8 | 148 |
| 4x2 Mixer | 4x2 | 16 | 156 |
|  |  |  | 172 |

### Algorithm #21  DPha -> 4TDly -> Pan

| Module |  | Size (bytes) | Offset |
| --- | --- | --- | --- |
| Dual Phaser | Dpha | 12 | 64 |
| 3x3 Mixer | 3x3 | 12 | 76 |
| 4 Tap Delay 1.4 Sec | 4TDly | 24 | 88 |
| 5x1 Mixer | 5x1 | 10 | 112 |
| 6x2 Mixer | 6x2 | 24 | 122 |
| Auto Panner | Pan | 8 | 146 |
| 4x2 Mixer | 4x2 | 16 | 154 |
|  |  |  | 170 |

### Algorithm #22  Gated Reverb

| Module |  | Size (bytes) | Offset |
| --- | --- | --- | --- |
| Gated Reverb | GtRvb | 22 | 64 |
| 3x2 Mixer | 3x2 | 12 | 86 |
|  |  |  | 98 |

### Algorithm #23  4Pcho -> 2TDly -> SDuc

| Module |  | Size (bytes) | Offset |
| --- | --- | --- | --- |
| 4 Phase Chorus | 4PCho | 18 | 64 |
| 5x3 Mixer | 5x3 | 20 | 82 |
| 2 Tap Delay 1.4 Sec | 2TDly | 16 | 102 |
| Stereo Ducker | SDuc | 12 | 118 |
| 4x2 Mixer | 4x2 | 16 | 130 |
|  |  |  | 146 |

### Algorithm #24  Chorus -> BigVerb

| Module |  | Size (bytes) | Offset |
| --- | --- | --- | --- |
| Mono Chorus | Cho | 12 | 64 |
| 2x3 Mixer | 2x3 | 8 | 76 |
| BigVerb | Big | 28 | 84 |
| 4x2 Mixer | 4x2 | 16 | 112 |
|  |  |  | 128 |

### Algorithm #25  Detune -> BigVerb

| Module |  | Size (bytes) | Offset |
| --- | --- | --- | --- |
| Mono Detune | Dtn | 8 | 64 |
| 2x3 Mixer | 2x3 | 8 | 72 |
| BigVerb | Big | 28 | 80 |
| 4x2 Mixer | 4x2 | 16 | 108 |
|  |  |  | 124 |

### Algorithm #26  Chorus -> BigVerb

| Module |  | Size (bytes) | Offset |
| --- | --- | --- | --- |
| Mono Flange | Fla | 14 | 64 |
| 2x3 Mixer | 2x1 | 4 | 78 |
| BigVerb | Big | 28 | 82 |
| 4x2 Mixer | 3x2 | 12 | 110 |
|  |  |  | 122 |

### Algorithm #27  Phaser -> BigVerb

| Module |  | Size (bytes) | Offset |
| --- | --- | --- | --- |
| Mono Phaser | Pha | 12 | 64 |
| 2x3 Mixer | 2x3 | 8 | 76 |
| BigVerb | Big | 28 | 84 |
| 4x2 Mixer | 4x2 | 16 | 112 |
|  |  |  | 128 |

### Algorithm #28  Dly -> Dual Chorus

| Module |  | Size (bytes) | Offset |
| --- | --- | --- | --- |
| Mono Delay 1.0 Sec | Dly | 12 | 64 |
| 2x1 Mixer | 2x1 | 4 | 76 |
| Dual Chorus | DCho | 14 | 80 |
| 4x2 Mixer | 4x2 | 16 | 94 |
|  |  |  | 110 |

### Algorithm #29  Dly -> Dual Detune

| Module |  | Size (bytes) | Offset |
| --- | --- | --- | --- |
| Mono Delay 1.0 Sec | Dly | 12 | 64 |
| 2x1 Mixer | 2x1 | 4 | 76 |
| Dual Detune | DDtn | 10 | 80 |
| 4x2 Mixer | 4x2 | 16 | 90 |
|  |  |  | 106 |

### Algorithm #30  Dly -> Dual Flange

| Module |  | Size (bytes) | Offset |
| --- | --- | --- | --- |
| Mono Delay 1.0 Sec | Dly | 12 | 64 |
| 2x1 Mixer | 2x1 | 4 | 76 |
| Dual Flange | DFla | 14 | 80 |
| 4x2 Mixer | 4x2 | 16 | 94 |
|  |  |  | 110 |

### Algorithm #31  Dly -> Dual Phaser

| Module |  | Size (bytes) | Offset |
| --- | --- | --- | --- |
| Mono Delay 1.0 Sec | Dly | 12 | 64 |
| 2x1 Mixer | 2x1 | 4 | 76 |
| Dual Phaser | DPha | 12 | 80 |
| 4x2 Mixer | 4x2 | 16 | 92 |
|  |  |  | 108 |

### Algorithm #32  Pitch -> 4TDly -> Pan

| Module |  | Size (bytes) | Offset |
| --- | --- | --- | --- |
| Mono Pitch Shift | Pch | 12 | 64 |
| 2x1 Mixer | 2x1 | 4 | 76 |
| 4 Tap Delay 1.4 Sec | 4TDly | 24 | 80 |
| 5x1 Mixer | 5x1 | 10 | 104 |
| 5x2 Mixer | 5x2 | 20 | 114 |
| Auto Panner | Pan | 8 | 134 |
| 4x2 Mixer | 4x2 | 16 | 142 |
|  |  |  | 158 |

### Algorithm #33  Wha -> Cho -> 2TDly -> Reverb

| Module |  | Size (bytes) | Offset |
| --- | --- | --- | --- |
| Traditional Wah | Twah | 6 | 64 |
| Mono Chorus | Cho | 12 | 72 |
| 2x1 Mixer | 2x1 | 4 | 84 |
| 2 Tap Delay 0.8 Sec | 2Tdly | 16 | 88 |
| 4x3 Mixer | 4x3 | 16 | 104 |
| MFX Reverb | MVRB | 18 | 120 |
| 4x2 Mixer | 4x2 | 18 | 138 |
|  |  |  | 156 |

### Algorithm #34  No Digital

| Module |  | Size (bytes) | Offset |
| --- | --- | --- | --- |
|  |  |  | 64 |

# Modules

## Analog

### Compressor

| Command | Inputs | Outputs | Used by Algorithms |
| --- | --- | --- | --- |
| Comp | 1 | 1 | All |
| Parameters | Range | MIDI Data |
|  | Min | Max | Bytes | Type |
| Comp On/Bypass | Bypass | On | 2 | bypassable |
| Comp Amount | 0 | 31 | 2 | compAmount |
| Comp Level | 0 | 7 | 2 | compLevel |
|  |  |  | 6 | TOTAL |

### Distortion

| Command | Inputs | Outputs | Used by Algorithms |
| --- | --- | --- | --- |
| Dist | 1 | 1 | All |
| Parameters | Range | MIDI Data |
|  | Min | Max | Bytes | Type |
| Dist On/Bypass | Bypass | On | 2 | bypassable |
| Dist Type | Clean Tube | Grunge | 2 | distType |
| Dist Gain | 0.0 | 11.0 | 2 | distGain |
| Clean Level | Mute | 12.0dB | 2 | levelCleanDist |
| Distortion Level | Mute | 12.0dB | 2 | levelCleanDist |
|  |  |  | 10 | TOTAL |

## Equalizers

### 10 Band Graphic Equalizer

| Command | Inputs | Outputs | Used by Algorithms |
| --- | --- | --- | --- |
| GEQ10 | 1 | 1 | 12 |
| Parameters | Range | MIDI Data |
|  | Min | Max | Bytes | Type |
| GEQ10 31.5 Hz | -15dB | 15db | 2 | eqGain |
| GEQ10 63 Hz | -15dB | 15db | 2 | eqGain |
| GEQ10 125 Hz | -15dB | 15db | 2 | eqGain |
| GEQ10 250 Hz | -15dB | 15db | 2 | eqGain |
| GEQ10 500 Hz | -15dB | 15db | 2 | eqGain |
| GEQ10 1 kHz | -15dB | 15db | 2 | eqGain |
| GEQ10 2 kHz | -15dB | 15db | 2 | eqGain |
| GEQ10 4 kHz | -15dB | 15db | 2 | eqGain |
| GEQ10 8 kHz | -15dB | 15db | 2 | eqGain |
| GEQ10 16 kHz | -15dB | 15db | 2 | eqGain |
| GEQ10 Level | 0 | 100 | 2 | levelBarGraph |
|  |  |  | 22 | TOTAL |

### 4 Band Parametric Equalizer

| Command | Inputs | Outputs | Used by Algorithms |
| --- | --- | --- | --- |
| PEQ | 1 | 1 | All |
| Parameters | Range | MIDI Data |
|  | Min | Max | Bytes | Type |
| PEQ Band1 Freq | 25Hz | 20000Hz | 2 | audibleHzRange |
| PEQ Band1 Q | .25 | 16.00 | 2 | eqQ |
| PEQ Band1 Gain | -15dB | 15db | 2 | eqGain |
| PEQ Band2 Freq | 25Hz | 20000Hz | 2 | audibleHzRange |
| PEQ Band2 Q | .25 | 16.00 | 2 | eqQ |
| PEQ Band2 Gain | -15dB | 15db | 2 | eqGain |
| PEQ Band3 Freq | 25Hz | 20000Hz | 2 | audibleHzRange |
| PEQ Band3 Q | .25 | 16.00 | 2 | eqQ |
| PEQ Band3 Gain | -15dB | 15db | 2 | eqGain |
| PEQ Band4 Freq | 25Hz | 20000Hz | 2 | audibleHzRange |
| PEQ Band4 Q | .25 | 16.00 | 2 | eqQ |
| PEQ Band4 Gain | -15dB | 15db | 2 | eqGain |
|  |  |  | 24 | TOTAL |

### Cabinet Emulator

| Command | Inputs | Outputs | Used by Algorithms |
| --- | --- | --- | --- |
| CabEm | 1 | 1 | All |
| Parameters | Range | MIDI Data |
|  | Min | Max | Bytes | Type |
| Cabinet Emulator | Bypass | On | 2 | bypassable |
| Cabinet Type | 1 Warm Cab | 10 Max Bndwidth | 2 | cabType |
|  |  |  | 4 | TOTAL |

## Reverbs

### Multi-FX Reverb

| Command | Inputs | Outputs | Used by Algorithms |
| --- | --- | --- | --- |
| MVerb | 1 | 2 | 1, 2, 3, 4, 5, 8, 14, 15 |
| Parameters | Range | MIDI Data |
|  | Min | Max | Bytes | Type |
| MFX Reverb | Off | On | 2 | moduleOnOff |
| Reverb Predelay | 0ms | 100ms | 2 | incDelay( 100, 1) |
| Reverb Spread | 10ms | 100ms | 2 | rvbSpread1 |
| Reverb Diffusion | 1 | 10 | 2 | inc( 1, 10 ) |
| RV Hi-Freq Decay | 25Hz | 20000Hz | 2 | audibleHzRange |
| RV Hi-FrqRollOff | 25Hz | 20000Hz | 2 | audibleHzRange |
| Reverb Size | 1 | 10 | 2 | inc( 1, 10 ) |
| Reverb RT60 | 0.01 Sec | 20.00 Sec | 2 | rvbRT( Reverb Size ) |
| Reverb Level | 0 | 100 | 2 | levelBarGraph |
|  |  |  | 18 | TOTAL |

### BigVerb

| Command | Inputs | Outputs | Used by Algorithms |
| --- | --- | --- | --- |
| Big | 1 | 2 | 16, 24, 25, 26, 27 |
| Parameters | Range | MIDI Data |
|  | Min | Max | Bytes | Type |
| BigVerb | Off | On | 2 | moduleOnOff |
| ER Predelay | 0ms | 100ms | 2 | incDelay( 100, 1) |
| ER Spread | 25ms | 300ms | 2 | rvbSpread2 |
| ER Shape | 1 | 10 | 2 | inc( 1, 10 ) |
| ER Diffusion | 1 | 10 | 2 | inc( 1, 10 ) |
| ER Level | 0 | 100 | 2 | levelBarGraph |
| RV Predelay | 1ms | 100ms | 2 | incDelay( 100, 1) |
| RV Spread | 20ms | 180ms | 2 | rvbSpread3 |
| RV Diffusion | 1 | 10 | 2 | inc( 1, 10 ) |
| RV Hi-Freq Decay | 25Hz | 20000Hz | 2 | audibleHzRange |
| RV Hi-FrqRollOff | 25Hz | 20000Hz | 2 | audibleHzRange |
| RV Size | 1 | 10 | 2 | inc( 1, 10 ) |
| RV RT60 | 0.01 Sec | 20.00 Sec | 2 | rvbRT( RV Size ) |
| RV Level | 0 | 100 | 2 | levelBarGraph |
|  |  |  | 28 | TOTAL |

### Gated Reverb

| Command | Inputs | Outputs | Used by Algorithms |
| --- | --- | --- | --- |
| GtRvb | 1 | 2 | 22 |
| Parameters | Range | MIDI Data |
|  | Min | Max | Bytes | Type |
| Gated Reverb | Off | On | 2 | moduleOnOff |
| Rvb Pre-delay | 0ms | 100ms | 2 | incDelay( 100, 1) |
| Rvb Decay Time | 20ms | 1000ms | 2 | rvbGatedDecay |
| Rvb Envelope | Decaying | Reverse | 2 | rvbGatedEnvelope |
| Rvb Diffusion | 1 | 10 | 2 | inc( 1, 10 ) |
| Rvb LPF Frequency | 25Hz | 20000Hz | 2 | audibleHzRange |
| Rvb Accent Delay | -50ms | 50ms | 2 | rvbAccentDelay |
| Rvb Accent Left | 0 | 100 | 2 | levelBarGraph |
| Rvb Accent Right | 0 | 100 | 2 | levelBarGraph |
| Rvb Level Left | 0 | 100 | 2 | levelBarGraph |
| Rvb Level Right | 0 | 100 | 2 | levelBarGraph |
|  |  |  | 22 | TOTAL |

## Delays/Sampler

### Mono Delay 1.0 Sec

| Command | Inputs | Outputs | Used by Algorithms |
| --- | --- | --- | --- |
| Dly | 1 | 1 | 8, 28, 29, 30, 31 |
| Parameters | Range | MIDI Data |
|  | Min | Max | Bytes | Type |
| Mono Delay 1.0s | Off | On | 2 | moduleOnOff |
| Delay Level | 0 | 100 | 2 | levelBarGraph |
| Delay Time | 0.000 | 1.000 | 4 | dlyDelay( 1.0 ) |
| Delay Feedback | Off | 99% | 2 | dlyFdBack |
| Delay Repeat Hld | Off | Hold | 2 | RptHld |
|  |  |  | 12 | TOTAL |

### 2 Tap Delay 0.4 Sec

| Command | Inputs | Outputs | Used by Algorithms |
| --- | --- | --- | --- |
| 2TDly | 1 | 2 | 11 |
| Parameters | Range | MIDI Data |
|  | Min | Max | Bytes | Type |
| 2 Tap Delay 0.4s | Off | On | 2 | moduleOnOff |
| Delay Level | 0 | 100 | 2 | levelBarGraph |
| Delay Time Tap 1 | 0.000 | 0.400 | 4 | dlyDelay( 0.4 ) |
| Delay Time Tap 2 | 0.000 | 0.400 | 4 | dlyDelay( 0.4 ) |
| Delay Feedback T2 | Off | 99% | 2 | dlyFdBack |
| Delay Repeat Hld | Off | Hold | 2 | RptHld |
|  |  |  | 16 | TOTAL |

### 2 Tap Delay 0.8 Sec

| Command | Inputs | Outputs | Used by Algorithms |
| --- | --- | --- | --- |
| 2TDly | 1 | 2 | 1, 2, 3, 4, 5, 15 |
| Parameters | Range | MIDI Data |
|  | Min | Max | Bytes | Type |
| 2 Tap Delay 0.8s | Off | On | 2 | moduleOnOff |
| Delay Level | 0 | 100 | 2 | levelBarGraph |
| Delay Time Tap 1 | 0.000 | 0.800 | 4 | dlyDelay( 0.8 ) |
| Delay Time Tap 2 | 0.000 | 0.800 | 4 | dlyDelay( 0.8 ) |
| Delay Feedback T2 | Off | 99% | 2 | dlyFdBack |
| Delay Repeat Hld | Off | Hold | 2 | RptHld |
|  |  |  | 16 | TOTAL |

### 2 Tap Delay 1.4 Sec

| Command | Inputs | Outputs | Used by Algorithms |
| --- | --- | --- | --- |
| 2TDly | 1 | 2 | 6, 9, 13, 23 |
| Parameters | Range | MIDI Data |
|  | Min | Max | Bytes | Type |
| 2 Tap Delay 1.4s | Off | On | 2 | moduleOnOff |
| Delay Level | 0 | 100 | 2 | levelBarGraph |
| Delay Time Tap 1 | 0.000 | 1.400 | 4 | dlyDelay( 1.4 ) |
| Delay Time Tap 2 | 0.000 | 1.400 | 4 | dlyDelay( 1.4 ) |
| Delay Feedback T2 | Off | 99% | 2 | dlyFdBack |
| Delay Repeat Hld | Off | Hold | 2 | RptHld |
|  |  |  | 16 | TOTAL |

### 4 Tap Delay 1.4 Sec

| Command | Inputs | Outputs | Used by Algorithms |
| --- | --- | --- | --- |
| 4TDly | 1 | 4 | 7, 18, 19, 20, 21, 32 |
| Parameters | Range | MIDI Data |
|  | Min | Max | Bytes | Type |
| 4 Tap Delay 1.4s | Off | On | 2 | moduleOnOff |
| Delay Level | 0 | 100 | 2 | levelBarGraph |
| Delay Time Tap 1 | 0.000 | 1.400 | 4 | dlyDelay( 1.4 ) |
| Delay Time Tap 2 | 0.000 | 1.400 | 4 | dlyDelay( 1.4 ) |
| Delay Time Tap 3 | 0.000 | 1.400 | 4 | dlyDelay( 1.4 ) |
| Delay Time Tap 4 | 0.000 | 1.400 | 4 | dlyDelay( 1.4 ) |
| Delay Feedback | Off | 99% | 2 | dlyFdBack |
| Delay Repeat Hld | Off | Hold | 2 | RptHld |
|  |  |  | 24 | TOTAL |

### Stereo Delay 0.5 Sec

| Command | Inputs | Outputs | Used by Algorithms |
| --- | --- | --- | --- |
| SDly | 2 | 2 | 10, 17 |
| Parameters | Range | MIDI Data |
|  | Min | Max | Bytes | Type |
| Stereo Delay 0.5s | Off | On | 2 | moduleOnOff |
| Delay Level | 0 | 100 | 2 | levelBarGraph |
| Delay Time | 0.000 | 0.500 | 4 | dlyDelay( 0.5 ) |
| Delay Feedback | Off | 99% | 2 | dlyFdBack |
| Delay Repeat Hld | Off | Hold | 2 | RptHld |
|  |  |  | 12 | TOTAL |

### Modulated Delay 0.8 Sec

| Command | Inputs | Outputs | Used by Algorithms |
| --- | --- | --- | --- |
| MDly | 1 | 1 | 14 |
| Parameters | Range | MIDI Data |
|  | Min | Max | Bytes | Type |
| Modulated Delay | Off | On | 2 | moduleOnOff |
| Delay Time | 0.000 | 0.800 | 4 | dlyDelay( 0.8 ) |
| Delay Feedback | -99% | 99% | 2 | regenFdback |
| Delay LFO Speed | 0.06Hz | 16.00Hz | 2 | LFOSpeed |
| Delay LFO Depth | 0.00ms | 30.00ms | 2 | incDelay( 30.00, 0.25 ) |
| Delay LFO Waveform | Sine | Exponential | 2 | LFOWaveform |
| Delay Level | 0 | 100 | 2 | levelBarGraph |
|  |  |  | 16 | TOTAL |

### Sampler

| Command | Inputs | Outputs | Used by Algorithms |
| --- | --- | --- | --- |
| Smpl | 1 | 1 | 12 |
| Parameters | Range | MIDI Data |
|  | Min | Max | Bytes | Type |
| Sampler 1.5 Sec. | Off | On | 2 | moduleOnOff |
| Sample Plybck Levl | 0 | 100 | 2 | levelBarGraph |
| Smpl Looping | Manual | Auto | 2 | smplLooping |
| Smpl Record/Pla | Record | Playback | 2 | smplRecordPlay |
| Smpl Manual Tri | ( Trigger | ( Trigger | 2 | smplManualTrigger |
| Smpl Trigger Mod | Manual Trig | Audio Re-Trig | 2 | smplTriggerMode |
| Smpl Triggr Levl | 0 | 100 | 2 | levelBarGraph |
| Smpl Direct Levl | 0 | 100 | 2 | levelBarGraph |
| Smpl Start Point | 0.000 | 1.499 | 4 | smplStartPoint( Smpl Stop Point ) |
| Smpl Stop Point | 0.001 | 1.500 | 4 | smplStopPoint( Smpl Start Point ) |
|  |  |  | 24 | TOTAL |

## Pitch Shifters

### Pitch Shifter

| Command | Inputs | Outputs | Used by Algorithms |
| --- | --- | --- | --- |
| Pch | 1 | 1 | 5, 7, 32 |
| Parameters | Range | MIDI Data |
|  | Min | Max | Bytes | Type |
| Pitch Shift | Off | On | 2 | moduleOnOff |
| Pitch Level | 0 | 100 | 2 | levelBarGraph |
| Pitch Shift Amnt | -24Tones | 24Tones | 2 | pchPitch |
| Pitch Detune | -100 Cents | 100 Cents | 2 | pchCents |
| Pitch Tracking | 0-100 Cents | 12-24 Tones | 2 | pchTrack |
| Pitch Regenerate | -99% | 99% | 2 | regenFdback |
|  |  |  | 12 | TOTAL |

### Mono Detuner

| Command | Inputs | Outputs | Used by Algorithms |
| --- | --- | --- | --- |
| Dtn | 1 | 1 | 25 |
| Parameters | Range | MIDI Data |
|  | Min | Max | Bytes | Type |
| Mono Detune | Off | On | 2 | moduleOnOff |
| Detune Level | 0 | 100 | 2 | levelBarGraph |
| Detune 1 Predly | 0ms | 100ms | 2 | incDelay( 100, 1 ) |
| Detune Amount | -100 Cents | 100 Cents | 2 | pchCents |
|  |  |  | 8 | TOTAL |

### Dual Detuner

| Command | Inputs | Outputs | Used by Algorithms |
| --- | --- | --- | --- |
| DDtn | 1 | 2 | 2, 19, 29 |
| Parameters | Range | MIDI Data |
|  | Min | Max | Bytes | Type |
| Dual Detune | Off | On | 2 | moduleOnOff |
| Detune Level | 0 | 100 | 2 | levelBarGraph |
| Detune 1 Predly | 0ms | 100ms | 2 | incDelay( 100, 1 ) |
| Detune 2 Predly | 0ms | 100ms | 2 | incDelay( 100, 1 ) |
| Detune Amount | -100 Cents | 100 Cents | 2 | pchCents |
|  |  |  | 10 | TOTAL |

### Arpeggiator

| Command | Inputs | Outputs | Used by Algorithms |
| --- | --- | --- | --- |
| Arp | 1 | 1 | 11 |
| Parameters | Range | MIDI Data |
|  | Min | Max | Bytes | Type |
| Arpeggiator | Off | On | 2 | moduleOnOff |
| Arpeggiator Level | 0 | 100 | 2 | levelBarGraph |
| Arp Pitch Shift | -24Tones | 24Tones | 2 | pchPitch |
| Arp Pitch Detune | -100 Cents | 100 Cents | 2 | pchCents |
| Arp Pch Tracking | 0-100 Cents | 12-24 Tones | 2 | pchTrack |
| Arpeggio Delay | 0.000 | 0.400 | 4 | dlyDelay( 0.4 ) |
| Arpeggio Feedbc | -99% | 99% | 2 | regenFdback |
|  |  |  | 16 | TOTAL |

### Whammy

| Command | Inputs | Outputs | Used by Algorithms |
| --- | --- | --- | --- |
| Wham | 1 | 1 | 11 |
| Parameters | Range | MIDI Data |
|  | Min | Max | Bytes | Type |
| Whammy | Off | On | 2 | moduleOnOff |
| Whammy Function | Shallow Detune | 12Below-12Abv | 2 | pchWhammyFunction |
| Whammy Pedal | 0 | 100 | 2 | inc( 0, 100 ) |
|  |  |  | 6 | TOTAL |

## Modulation

### Mono Chorus

| Command | Inputs | Outputs | Used by Algorithms |
| --- | --- | --- | --- |
| Cho | 1 | 1 | 7, 24 |
| Parameters | Range | MIDI Data |
|  | Min | Max | Bytes | Type |
| Mono Chorus | Off | On | 2 | moduleOnOff |
| Chorus Level | 0 | 100 | 2 | levelBarGraph |
| Chorus Speed | 0.06Hz | 16.00Hz | 2 | LFOSpeed |
| Chorus Depth | 0.00ms | 30.00ms | 2 | incDelay( 30.00, 0.25 ) |
| Chorus Delay | 0.00ms | 60.00ms | 2 | incDelay( 60.00, 0.25 ) |
| Chorus Waveform | Sine | Exponential | 2 | LFOWaveform |
|  |  |  | 12 | TOTAL |

### Dual Chorus

| Command | Inputs | Outputs | Used by Algorithms |
| --- | --- | --- | --- |
| DCho | 1 | 2 | 1, 6, 9, 10, 13, 18, 28 |
| Parameters | Range | MIDI Data |
|  | Min | Max | Bytes | Type |
| Dual Chorus | Off | On | 2 | moduleOnOff |
| Chorus Level | 0 | 100 | 2 | levelBarGraph |
| Chorus Speed | 0.06Hz | 16.00Hz | 2 | LFOSpeed |
| Chorus Depth | 0.00ms | 30.00ms | 2 | incDelay( 30.00, 0.25 ) |
| Chorus Delay 1 | 0.00ms | 60.00ms | 2 | incDelay( 60.00, 0.25 ) |
| Chorus Delay 2 | 0.00ms | 60.00ms | 2 | incDelay( 60.00, 0.25 ) |
| Chorus Waveform | Sine | Exponential | 2 | LFOWaveform |
|  |  |  | 14 | TOTAL |

### 4 Phase Chorus

| Command | Inputs | Outputs | Used by Algorithms |
| --- | --- | --- | --- |
| 4PCho | 1 | 4 | 13, 17, 23 |
| Parameters | Range | MIDI Data |
|  | Min | Max | Bytes | Type |
| 4 Phase Chorus | Off | On | 2 | moduleOnOff |
| Chorus Level | 0 | 100 | 2 | levelBarGraph |
| Chorus Speed | 0.06Hz | 16.00Hz | 2 | LFOSpeed |
| Chorus Depth | 0.00ms | 30.00ms | 2 | incDelay( 30.00, 0.25 ) |
| Chorus Delay 1 | 0.00ms | 60.00ms | 2 | incDelay( 60.00, 0.25 ) |
| Chorus Delay 2 | 0.00ms | 60.00ms | 2 | incDelay( 60.00, 0.25 ) |
| Chorus Delay 3 | 0.00ms | 60.00ms | 2 | incDelay( 60.00, 0.25 ) |
| Chorus Delay 4 | 0.00ms | 60.00ms | 2 | incDelay( 60.00, 0.25 ) |
|  |  |  | 16 | TOTAL |

### Mono Flange

| Command | Inputs | Outputs | Used by Algorithms |
| --- | --- | --- | --- |
| Fla | 1 | 1 | 26 |
| Parameters | Range | MIDI Data |
|  | Min | Max | Bytes | Type |
| Mono Flange | Off | On | 2 | moduleOnOff |
| Flange Level | 0 | 100 | 2 | levelBarGraph |
| Flange Delay | 0.0ms | 10.0ms | 2 | incDelay( 10.0, 0.1 ) |
| Flange Feedback | -99% | 99% | 2 | regenFdback |
| Flange Speed | 0.06Hz | 16.00Hz | 2 | LFOSpeed |
| Flange Depth | 0.00ms | 30.00ms | 2 | incDelay( 30.00, 0.25 ) |
| Flange Waveform | Sine | Exponential | 2 | LFOWaveform |
|  |  |  | 14 | TOTAL |

### Dual Flange

| Command | Inputs | Outputs | Used by Algorithms |
| --- | --- | --- | --- |
| DFla | 1 | 2 | 3, 20, 30 |
| Parameters | Range | MIDI Data |
|  | Min | Max | Bytes | Type |
| Dual Flange | Off | On | 2 | moduleOnOff |
| Flange Level | 0 | 100 | 2 | levelBarGraph |
| Flange Delay | 0.00ms | 60.00ms | 2 | incDelay( 60.00, 0.25 ) |
| Flange Feedback | -99% | 99% | 2 | regenFdback |
| Flange Speed | 0.06Hz | 16.00Hz | 2 | LFOSpeed |
| Flange Depth | 0.00ms | 30.00ms | 2 | incDelay( 30.00, 0.25 ) |
| Flange Waveform | Sine | Exponential | 2 | LFOWaveform |
|  |  |  | 14 | TOTAL |

### Mono Phaser

| Command | Inputs | Outputs | Used by Algorithms |
| --- | --- | --- | --- |
| Pha | 1 | 1 | 27 |
| Parameters | Range | MIDI Data |
|  | Min | Max | Bytes | Type |
| Mono Phaser | Off | On | 2 | moduleOnOff |
| Phaser Level | 0 | 100 | 2 | levelBarGraph |
| Phaser Regenertn | -99% | 99% | 2 | regenFdback |
| Phaser Speed | 0.06Hz | 16.00Hz | 2 | LFOSpeed |
| Phaser Depth | 0 | 100 | 2 | levelBarGraph |
| Phaser Waveform | Sine | Exponential | 2 | LFOWaveform |
|  |  |  | 12 | TOTAL |

### Dual Phaser

| Command | Inputs | Outputs | Used by Algorithms |
| --- | --- | --- | --- |
| DPha | 1 | 2 | 4, 21, 31 |
| Parameters | Range | MIDI Data |
|  | Min | Max | Bytes | Type |
| Dual Phaser | Off | On | 2 | moduleOnOff |
| Phaser Level | 0 | 100 | 2 | levelBarGraph |
| Phaser Regenertn | -99% | 99% | 2 | regenFdback |
| Phaser Speed | 0.06Hz | 16.00Hz | 2 | LFOSpeed |
| Phaser Depth | 0 | 100 | 2 | levelBarGraph |
| Phaser Waveform | Sine | Exponential | 2 | LFOWaveform |
|  |  |  | 12 | TOTAL |

### Mono Tremolo

| Command | Inputs | Outputs | Used by Algorithms |
| --- | --- | --- | --- |
| Trm | 1 | 1 | 4 |
| Parameters | Range | MIDI Data |
|  | Min | Max | Bytes | Type |
| Mono Tremolo | Off | On | 2 | moduleOnOff |
| Tremolo Level | 0 | 100 | 2 | levelBarGraph |
| Tremolo Speed | 0.06Hz | 16.00Hz | 2 | LFOSpeed |
| Tremolo Depth | 1 | 100 | 2 | inc( 1, 100 ) |
|  |  |  | 8 | TOTAL |

### Stereo Tremolo

| Command | Inputs | Outputs | Used by Algorithms |
| --- | --- | --- | --- |
| STrm | 2 | 2 | 9 |
| Parameters | Range | MIDI Data |
|  | Min | Max | Bytes | Type |
| Stereo Tremolo | Off | On | 2 | moduleOnOff |
| Tremolo Level | 0 | 100 | 2 | levelBarGraph |
| Tremolo Speed | 0.06Hz | 16.00Hz | 2 | LFOSpeed |
| Tremolo Depth | 1 | 100 | 2 | inc( 1, 100 ) |
|  |  |  | 8 | TOTAL |

### Auto Panner

| Command | Inputs | Outputs | Used by Algorithms |
| --- | --- | --- | --- |
| Pan | 1 | 2 | 6, 18, 19, 20, 21, 32 |
| Parameters | Range | MIDI Data |
|  | Min | Max | Bytes | Type |
| Auto Panner | Off | On | 2 | moduleOnOff |
| Panner Level | 0 | 100 | 2 | levelBarGraph |
| Panner Speed | 0.06Hz | 16.00Hz | 2 | LFOSpeed |
| Panner Depth | 1 | 100 | 2 | panDepth |
|  |  |  | 8 | TOTAL |

## Mixers

### 2x1 Mixer

| Command | Inputs | Outputs | Used by Algorithms |
| --- | --- | --- | --- |
| 2x1 | 2 | 1 | 5, 7, 8, 26, 28, 29, 30, 31, 32, 34, 35, 36 |
| Parameters | Range | MIDI Data |
|  | Min | Max | Bytes | Type |
| 2x1 In 1 Level | 0 | 100 | 2 | levelBarGraph |
| 2x1 In 2 Level | 0 | 100 | 2 | levelBarGraph |
|  |  |  | 4 | TOTAL |

### 3x1 Mixer

| Command | Inputs | Outputs | Used by Algorithms |
| --- | --- | --- | --- |
| 3x1 | 3 | 1 | 6, 15 |
| Parameters | Range | MIDI Data |
|  | Min | Max | Bytes | Type |
| 3x1 In 1 Level | 0 | 100 | 2 | levelBarGraph |
| 3x1 In 2 Level | 0 | 100 | 2 | levelBarGraph |
| 3x1 In 3 Level | 0 | 100 | 2 | levelBarGraph |
|  |  |  | 6 | TOTAL |

### 5x1 Mixer

| Command | Inputs | Outputs | Used by Algorithms |
| --- | --- | --- | --- |
| 5x1 | 5 | 1 | 18, 19, 20, 21, 32 |
| Parameters | Range | MIDI Data |
|  | Min | Max | Bytes | Type |
| 5x1 In 1 Level | 0 | 100 | 2 | levelBarGraph |
| 5x1 In 2 Level | 0 | 100 | 2 | levelBarGraph |
| 5x1 In 3 Level | 0 | 100 | 2 | levelBarGraph |
| 5x1 In 4 Level | 0 | 100 | 2 | levelBarGraph |
| 5x1 In 5 Level | 0 | 100 | 2 | levelBarGraph |
|  |  |  | 10 | TOTAL |

### 3x2 Mixer

| Command | Inputs | Outputs | Used by Algorithms |
| --- | --- | --- | --- |
| 3x2 | 3 | 2 | 5, 8, 9, 10, 13, 16, 22, 26 |
| Parameters | Range | MIDI Data |
|  | Min | Max | Bytes | Type |
| 3x2 In 1 Level | 0 | 100 | 2 | levelBarGraph |
| 3x2 In 1 Pan | All Left | All Right | 2 | mixPanbarGraph |
| 3x2 In 2 Level | 0 | 100 | 2 | levelBarGraph |
| 3x2 In 2 Pan | All Left | All Right | 2 | mixPanbarGraph |
| 3x2 In 3 Level | 0 | 100 | 2 | levelBarGraph |
| 3x2 In 3 Pan | All Left | All Right | 2 | mixPanbarGraph |
|  |  |  | 12 | TOTAL |

### 4x2 Mixer

| Command | Inputs | Outputs | Used by Algorithms |
| --- | --- | --- | --- |
| 4x2 | 4 | 2 | 1, 2, 3, 4, 10, 11, 14, 18, 19, 20, 21, 23, 24, 25, 27,28, 29, 30, 31, 32 |
| Parameters | Range | MIDI Data |
|  | Min | Max | Bytes | Type |
| 4x2 In 1 Level | 0 | 100 | 2 | levelBarGraph |
| 4x2 In 1 Pan | All Left | All Right | 2 | mixPanbarGraph |
| 4x2 In 2 Level | 0 | 100 | 2 | levelBarGraph |
| 4x2 In 2 Pan | All Left | All Right | 2 | mixPanbarGraph |
| 4x2 In 3 Level | 0 | 100 | 2 | levelBarGraph |
| 4x2 In 3 Pan | All Left | All Right | 2 | mixPanbarGraph |
| 4x2 In 4 Level | 0 | 100 | 2 | levelBarGraph |
| 4x2 In 4 Pan | All Left | All Right | 2 | mixPanbarGraph |
|  |  |  | 18 | TOTAL |

### 5x2 Mixer

| Command | Inputs | Outputs | Used by Algorithms |
| --- | --- | --- | --- |
| 5x2 | 5 | 2 | 6, 7, 9, 15, 17 |
| Parameters | Range | MIDI Data |
|  | Min | Max | Bytes | Type |
| 5x2 In 1 Level | 0 | 100 | 2 | levelBarGraph |
| 5x2 In 1 Pan | All Left | All Right | 2 | mixPanbarGraph |
| 5x2 In 2 Level | 0 | 100 | 2 | levelBarGraph |
| 5x2 In 2 Pan | All Left | All Right | 2 | mixPanbarGraph |
| 5x2 In 3 Level | 0 | 100 | 2 | levelBarGraph |
| 5x2 In 3 Pan | All Left | All Right | 2 | mixPanbarGraph |
| 5x2 In 4 Level | 0 | 100 | 2 | levelBarGraph |
| 5x2 In 4 Pan | All Left | All Right | 2 | mixPanbarGraph |
| 5x2 In 5 Level | 0 | 100 | 2 | levelBarGraph |
| 5x2 In 5 Pan | All Left | All Right | 2 | mixPanbarGraph |
|  |  |  | 20 | TOTAL |

### 6x2 Mixer

| Command | Inputs | Outputs | Used by Algorithms |
| --- | --- | --- | --- |
| 6x2 | 6 | 2 | 18, 19, 20, 21 |
| Parameters | Range | MIDI Data |
|  | Min | Max | Bytes | Type |
| 6x2 In 1 Level | 0 | 100 | 2 | levelBarGraph |
| 6x2 In 1 Pan | All Left | All Right | 2 | mixPanbarGraph |
| 6x2 In 2 Level | 0 | 100 | 2 | levelBarGraph |
| 6x2 In 2 Pan | All Left | All Right | 2 | mixPanbarGraph |
| 6x2 In 3 Level | 0 | 100 | 2 | levelBarGraph |
| 6x2 In 3 Pan | All Left | All Right | 2 | mixPanbarGraph |
| 6x2 In 4 Level | 0 | 100 | 2 | levelBarGraph |
| 6x2 In 4 Pan | All Left | All Right | 2 | mixPanbarGraph |
| 6x2 In 5 Level | 0 | 100 | 2 | levelBarGraph |
| 6x2 In 5 Pan | All Left | All Right | 2 | mixPanbarGraph |
| 6x2 In 6 Level | 0 | 100 | 2 | levelBarGraph |
| 6x2 In 6 Pan | All Left | All Right | 2 | mixPanbarGraph |
|  |  |  | 24 | TOTAL |

### 7x2 Mixer

| Command | Inputs | Outputs | Used by Algorithms |
| --- | --- | --- | --- |
| 7x2 | 7 | 2 | 6 |
| Parameters | Range | MIDI Data |
|  | Min | Max | Bytes | Type |
| 7x2 In 1 Level | 0 | 100 | 2 | levelBarGraph |
| 7x2 In 1 Pan | All Left | All Right | 2 | mixPanbarGraph |
| 7x2 In 2 Level | 0 | 100 | 2 | levelBarGraph |
| 7x2 In 2 Pan | All Left | All Right | 2 | mixPanbarGraph |
| 7x2 In 3 Level | 0 | 100 | 2 | levelBarGraph |
| 7x2 In 3 Pan | All Left | All Right | 2 | mixPanbarGraph |
| 7x2 In 4 Level | 0 | 100 | 2 | levelBarGraph |
| 7x2 In 4 Pan | All Left | All Right | 2 | mixPanbarGraph |
| 7x2 In 5 Level | 0 | 100 | 2 | levelBarGraph |
| 7x2 In 5 Pan | All Left | All Right | 2 | mixPanbarGraph |
| 7x2 In 6 Level | 0 | 100 | 2 | levelBarGraph |
| 7x2 In 6 Pan | All Left | All Right | 2 | mixPanbarGraph |
| 7x2 In 7 Level | 0 | 100 | 2 | levelBarGraph |
| 7x2 In 7 Pan | All Left | All Right | 2 | mixPanbarGraph |
|  |  |  | 28 | TOTAL |

### 8x2 Mixer

| Command | Inputs | Outputs | Used by Algorithms |
| --- | --- | --- | --- |
| 8x2 | 8 | 2 | 13 |
| Parameters | Range | MIDI Data |
|  | Min | Max | Bytes | Type |
| 8x2 In 1 Level | 0 | 100 | 2 | levelBarGraph |
| 8x2 In 1 Pan | All Left | All Right | 2 | mixPanbarGraph |
| 8x2 In 2 Level | 0 | 100 | 2 | levelBarGraph |
| 8x2 In 2 Pan | All Left | All Right | 2 | mixPanbarGraph |
| 8x2 In 3 Level | 0 | 100 | 2 | levelBarGraph |
| 8x2 In 3 Pan | All Left | All Right | 2 | mixPanbarGraph |
| 8x2 In 4 Level | 0 | 100 | 2 | levelBarGraph |
| 8x2 In 4 Pan | All Left | All Right | 2 | mixPanbarGraph |
| 8x2 In 5 Level | 0 | 100 | 2 | levelBarGraph |
| 8x2 In 5 Pan | All Left | All Right | 2 | mixPanbarGraph |
| 8x2 In 6 Level | 0 | 100 | 2 | levelBarGraph |
| 8x2 In 6 Pan | All Left | All Right | 2 | mixPanbarGraph |
| 8x2 In 7 Level | 0 | 100 | 2 | levelBarGraph |
| 8x2 In 7 Pan | All Left | All Right | 2 | mixPanbarGraph |
| 8x2 In 8 Level | 0 | 100 | 2 | levelBarGraph |
| 8x2 In 8 Pan | All Left | All Right | 2 | mixPanbarGraph |
|  |  |  | 32 | TOTAL |

### 2x3 Mixer

| Command | Inputs | Outputs | Used by Algorithms |
| --- | --- | --- | --- |
| 2x3 | 2 | 3 | 14, 24, 25, 26, 27 |
| Parameters | Range | MIDI Data |
|  | Min | Max | Bytes | Type |
| 2x3 In 1 Level | 0 | 100 | 2 | levelBarGraph |
| 2x3 In 1 Pan | All Left | All Right | 2 | mixPanbarGraph |
| 2x3 In 2 Level | 0 | 100 | 2 | levelBarGraph |
| 2x3 In 2 Pan | All Left | All Right | 2 | mixPanbarGraph |
|  |  |  | 8 | TOTAL |

### 3x3 Mixer

| Command | Inputs | Outputs | Used by Algorithms |
| --- | --- | --- | --- |
| 3x3 | 3 | 3 | 1, 2, 3, 4, 11, 18, 19, 20, 21 |
| Parameters | Range | MIDI Data |
|  | Min | Max | Bytes | Type |
| 3x3 In 1 Level | 0 | 100 | 2 | levelBarGraph |
| 3x3 In 1 Pan | All Left | All Right | 2 | mixPanbarGraph |
| 3x3 In 2 Level | 0 | 100 | 2 | levelBarGraph |
| 3x3 In 2 Pan | All Left | All Right | 2 | mixPanbarGraph |
| 3x3 In 3 Level | 0 | 100 | 2 | levelBarGraph |
| 3x3 In 3 Pan | All Left | All Right | 2 | mixPanbarGraph |
|  |  |  | 12 | TOTAL |

### 4x3 Mixer

| Command | Inputs | Outputs | Used by Algorithms |
| --- | --- | --- | --- |
| 4x3 | 4 | 3 | 1, 2, 3, 4 |
| Parameters | Range | MIDI Data |
|  | Min | Max | Bytes | Type |
| 4x3 In 1 Level | 0 | 100 | 2 | levelBarGraph |
| 4x3 In 1 Pan | All Left | All Right | 2 | mixPanbarGraph |
| 4x3 In 2 Level | 0 | 100 | 2 | levelBarGraph |
| 4x3 In 2 Pan | All Left | All Right | 2 | mixPanbarGraph |
| 4x3 In 3 Level | 0 | 100 | 2 | levelBarGraph |
| 4x3 In 3 Pan | All Left | All Right | 2 | mixPanbarGraph |
| 4x3 In 4 Level | 0 | 100 | 2 | levelBarGraph |
| 4x3 In 4 Pan | All Left | All Right | 2 | mixPanbarGraph |
|  |  |  | 16 | TOTAL |

### 5x3 Mixer

| Command | Inputs | Outputs | Used by Algorithms |
| --- | --- | --- | --- |
| 5x2 | 5 | 3 | 23 |
| Parameters | Range | MIDI Data |
|  | Min | Max | Bytes | Type |
| 5x3 In 1 Level | 0 | 100 | 2 | levelBarGraph |
| 5x3 In 1 Pan | All Left | All Right | 2 | mixPanbarGraph |
| 5x3 In 2 Level | 0 | 100 | 2 | levelBarGraph |
| 5x3 In 2 Pan | All Left | All Right | 2 | mixPanbarGraph |
| 5x3 In 3 Level | 0 | 100 | 2 | levelBarGraph |
| 5x3 In 3 Pan | All Left | All Right | 2 | mixPanbarGraph |
| 5x3 In 4 Level | 0 | 100 | 2 | levelBarGraph |
| 5x3 In 4 Pan | All Left | All Right | 2 | mixPanbarGraph |
| 5x3 In 5 Level | 0 | 100 | 2 | levelBarGraph |
| 5x3 In 5 Pan | All Left | All Right | 2 | mixPanbarGraph |
|  |  |  | 20 | TOTAL |

### Mixers

| Command | Inputs | Outputs | Used by Algorithms |
| --- | --- | --- | --- |
| Mixers | - | - | All |
| Parameters | Range | MIDI Data |
|  | Min | Max | Bytes | Type |
| Mixers | Hidden | Displayed | 2 | mixersDisplay |
|  |  |  | 2 | TOTAL |

### Master Mix

| Command | Inputs | Outputs | Used by Algorithms |
| --- | --- | --- | --- |
| MMIX | 1 | 1 | All |
| Parameters | Range | MIDI Data |
|  | Min | Max | Bytes | Type |
| Master Mix | All Dry | All Wet | 2 | wetDry |
|  |  |  | 2 | TOTAL |

## More

### Noise Gate

| Command | Inputs | Outputs | Used by Algorithms |
| --- | --- | --- | --- |
| NGt | 1 | 1 | All |
| Parameters | Range | MIDI Data |
|  | Min | Max | Bytes | Type |
| Noise Gate | Off | On | 2 | moduleOnOff |
| NG Threshold | -Infinity | +Infinity | 2 | ngtThreshold |
| NG Hold Time | 0ms | 500ms | 2 | ngtHoldTime |
| NG Attack Time | 0ms | 2000ms | 2 | ngtAttackRelease |
| NG Release Time | 0ms | 2000ms | 2 | ngtAttackRelease |
| NG Attenuation | 0dB | 100dB | 2 | ngtAttenuation |
| NG Delay Time | 0.0ms | 10.0ms | 2 | incDelay( 10.0, 0.1 ) |
|  |  |  | 14 | TOTAL |

### Stereo Ducker

| Command | Inputs | Outputs | Used by Algorithms |
| --- | --- | --- | --- |
| Duc | 3 | 2 | 8, 23 |
| Parameters | Range | MIDI Data |
|  | Min | Max | Bytes | Type |
| Stereo Ducker | Off | On | 2 | moduleOnOff |
| Duc Threshold | -100dB | 0dB | 2 | ducThreshAttn |
| Duc Hold Time | 0.000 | 5.000 | 2 | ducTime |
| Duc Attenuation | -100dB | 0dB | 2 | ducThreshAttn |
| Duc Attack Rate | 0.000 | 5.000 | 2 | ducTime |
| Duc Release Rate | 0.000 | 5.000 | 2 | ducTime |
|  |  |  | 12 | TOTAL |

### Phase Inverter

| Command | Inputs | Outputs | Used by Algorithms |
| --- | --- | --- | --- |
| Inv | 1 | 1 | 12 |
| Parameters | Range | MIDI Data |
|  | Min | Max | Bytes | Type |
| Phase Inverter | In Phase | Out Of Phase | 2 | otherPhase |
| Phase Inv Level | 0 | 100 | 2 | levelBarGraph |
|  |  |  | 4 | TOTAL |

### Traditional Wah

| Command | Inputs | Outputs | Used by Algorithms |
| --- | --- | --- | --- |
| TWah | 1 | 1 | 10, 16 |
| Parameters | Range | MIDI Data |
|  | Min | Max | Bytes | Type |
| Twah | Bypass | On | 2 | bypassable |
| Wah Level | 0 | 100 | 2 | levelBarGraph |
| WahPedalPositio | 0 | 127 | 2 | inc( 0, 127) |
|  |  |  | 6 | TOTAL |

### Automatic Wah

| Command | Inputs | Outputs | Used by Algorithms |
| --- | --- | --- | --- |
| AWah | 1 | 1 | 17 |
| Parameters | Range | MIDI Data |
|  | Min | Max | Bytes | Type |
| AutoWah | Bypass | On | 2 | bypassable |
| AutoWah Level | 0 | 100 | 2 | levelBarGraph |
| Awah Sensitivit | 0 | 100 | 2 | levelBarGraph |
|  |  |  | 6 | TOTAL |

### Master Level

| Command | Inputs | Outputs | Used by Algorithms |
| --- | --- | --- | --- |
| MLvl | 1 | 1 | All |
| Parameters | Range | MIDI Data |
|  | Min | Max | Bytes | Type |
| DSP Master Leve | 0 | 100 | 2 | levelBarGraph |
|  |  |  | 2 | TOTAL |

# Parameter Data

(Alphabetical Order)

### audibleHzRange

| SAP | MIDI |
| --- | --- |
| 25Hz | 0 |
| 32Hz | 1 |
| 40Hz | 2 |
| 50Hz | 3 |
| 63Hz | 4 |
| 80Hz | 5 |
| 100Hz | 6 |
| 125Hz | 7 |
| 160Hz | 8 |
| 200Hz | 9 |
| 250Hz | 10 |
| 315Hz | 11 |
| 400Hz | 12 |
| 500Hz | 13 |
| 630Hz | 14 |
| 800Hz | 15 |
| 1000Hz | 16 |
| 1250Hz | 17 |
| 1600Hz | 18 |
| 2000Hz | 19 |
| 2500Hz | 20 |
| 3150Hz | 21 |
| 4000Hz | 22 |
| 5000Hz | 23 |
| 6300Hz | 24 |
| 8000Hz | 25 |
| 10000Hz | 26 |
| 12500Hz | 27 |
| 16000Hz | 28 |
| 20000Hz | 29 |

bypassable

| SAP | MIDI |
| --- | --- |
| Bypass | 0 |
| On | 1 |

### cabType

| SAP | MIDI |
| --- | --- |
| 1 Warm Cab | 0 |
| 2 Warm Cab | 1 |
| 3 Warm Cab | 2 |
| 4 Med Cab | 3 |
| 5 Med Cab | 4 |
| 6 Med Cab | 5 |
| 7 Bright Cab | 6 |
| 8 Bright Cab | 7 |
| 9 Bright Cab | 8 |
| 10 MaxBndwidth | 9 |

### compAmount

| SAP | MIDI |
| --- | --- |
| 0 | 0 |
| x (x=0 to 31 by 1) | x |
| 31 | 31 |

### compLevel

| SAP | MIDI |
| --- | --- |
| 1 | 0 |
| x (x=1 to 7 by 1) | x-1 |
| 7 | 6 |

### distGain

| SAP | MIDI |
| --- | --- |
| 0.0 | 0 |
| x (x=0.0 to 11.0 by 0.5) | 2*x |
| 11.0 | 22 |

### distType

| SAP | MIDI |
| --- | --- |
| Clean Tube | 0 |
| Distorted Tube | 1 |
| Saturated Tube | 2 |
| Overdrive | 3 |
| Heavy Sustain | 4 |
| Grunge | 5 |

### dlyDelay( MaxDly )

| SAP | MIDI - 2 words 1st = 100’s 2nd = 10’s/1’s |
| --- | --- |
| 0.000 | 0 = 0, 0 |
| x (x=0.000 to MaxDly by 0.001) | x/0.1, x/0.001 mod 100 |
| x (x=MaxDly=0.400) | 400 = 4, 00 |
| x (x=MaxDly=0.500) | 500 = 5, 00 |
| x (x=MaxDly=0.800) | 800 = 8, 00 |
| x (x=MaxDly=1.000) | 1000 = 10, 00 |
| x (x=MaxDly=1.400) | 1400 = 14, 00 |

### dlyFdback

| SAP | MIDI |
| --- | --- |
| Off | 0 |
| x % (x=1 to 99 by 1) | x |
| 99 % | 99 |

### dlyHold

| SAP | MIDI |
| --- | --- |
| Off | 0 |
| Hold | 1 |

### ducThreshAttn

| SAP | MIDI |
| --- | --- |
| -100dB | 0 |
| xdB (x=-100 to 0 by 1) | x+100 |
| 0dB | 100 |

### ducTime

| SAP | MIDI |
| --- | --- |
| 0.000 | 0 |
| x (x=0.000 to 0.100 by 0.001) | x/0.001 |
| 0.100 | 100 |
| x (x=0.100 to 1.000 by 0.010) | (x-0.100)/ 0.010+100 |
| 1.000 | 190 |
| x (x=1.000 to 5.000 by 0.100) | (x-1.000)/ 0.100+190 |
| 5.000 | 230 |

### eqGain

| SAP | MIDI |
| --- | --- |
| -15db | 0 |
| xdb (x=-15 to 15 by 1) | x+15 |
| 0db | 15 |
| 15db | 30 |

### eqQ

| SAP | MIDI |
| --- | --- |
| .25 | 0 |
| .50 | 1 |
| .75 | 2 |
| 1.00 | 3 |
| 1.25 | 4 |
| 1.50 | 5 |
| 2.00 | 6 |
| 4.00 | 7 |
| 8.00 | 8 |
| 16.00 | 9 |

### inc( Min, Max )

| SAP | MIDI |
| --- | --- |
| x (x=Min=0) | 0 |
| x (x=Min=1) | 0 |
| x (x=Min to Max by 1) | x-Min |
| x (x=Max=10, Min=1) | 9 |
| x (x=Max=10, Min=0) | 10 |
| x (x=Max=100, Min=1) | 99 |
| x (x=Max=100, Min=0) | 100 |
| x (x=Max=127, Min=0) | 127 |

### incDelay( MaxDelay, Increment)

| SAP | MIDI |
| --- | --- |
| 0ms | 0 |
| xms (x=0 to MaxDelay by Increment) | x/Increment |
| xms (x=MaxDelay=100, Increment=1) | 100 |
| xms (x=MaxDelay=10.0, Increment=0.1) | 100 |
| xms (x=MaxDelay=30.0, Increment=0.25) | 120 |
| xms (x=MaxDelay=60.00, Increment=0.25) | 240 |

### levelBarGraph

| SAP | MIDI |
| --- | --- |
| 0 | 0 |
| x | x |
| 100 | 100 |

### levelCleanDist

| SAP | MIDI |
| --- | --- |
| Mute | 0 |
| -60 dB | 1 |
| -50 dB | 2 |
| -40 dB | 3 |
| -38 dB | 4 |
| -36 dB | 5 |
| x dB (x=-36 to -4 by 1) | x+36+5 |
| -4 dB | 37 |
| x dB (x=-3.5 to 0.0 by 0.5) | (x+4)/0.5+37 |
| 0 dB | 45 |
| x dB (x=0 to 12.0 by 0.5) | x/0.5+45 |
| 12 dB | 69 |

### LFOSpeed

| SAP | MIDI |
| --- | --- |
| 0.06Hz | 0 |
| xHz (x=0.06 to 1.00 by 0.01) | (x-0.06)/0.01 |
| 1.00Hz | 94 |
| xHz (x=1.00 to 16.00 by 0.10) | (x-1.00) /0.10+94 |
| 16.00Hz | 244 |

### LFOWaveform

| SAP | MIDI |
| --- | --- |
| Sine | 0 |
| Triangle | 1 |
| Logarithmic | 2 |
| Exponential | 3 |

### mixersDisplay

| SAP | MIDI |
| --- | --- |
| Hidden | 0 |
| Displayed | 1 |

### mixPanbarGraph

| SAP | MIDI |
| --- | --- |
| All Left | 0 |
| x (x=-12 to +12) | x+13 |
| 0 | 13 |
| All Right | 26 |

### moduleOnOff

| SAP | MIDI |
| --- | --- |
| Off | 0 |
| On | 1 |

### ngtAttackRelease

| SAP | MIDI |
| --- | --- |
| 0ms | 0 |
| xms (x=0 to 20 by 1) | x |
| 20ms | 20 |
| xms (x=20 to 200 by 5) | (x-20)/5+20 |
| 200ms | 56 |
| xms (x=200 to 2000 by 50) | (x-200)/50+56 |
| 2000ms | 92 |

### ngtAttenuation

| SAP | MIDI |
| --- | --- |
| 0dB | 0 |
| xdB (x=0 to 30 by 1) | x |
| 30dB | 30 |
| xdB (x= 30 to 90 by 3) | (x-30)/3+30 |
| 90dB | 50 |
| 100dB | 51 |

### ngtHoldTime

| SAP | MIDI |
| --- | --- |
| 0ms | 0 |
| xms (x=0 to 500 by 2) | x/2 |
| 500ms | 250 |

### ngtThreshold

| SAP | MIDI |
| --- | --- |
| - Infinity | 0 |
| -84 dB | 1 |
| -81 dB | 2 |
| -78 dB | 3 |
| -75 dB | 4 |
| -72 dB | 5 |
| -69 dB | 6 |
| -66 dB | 7 |
| -63 dB | 8 |
| -59 dB | 9 |
| -56 dB | 10 |
| -53 dB | 11 |
| -50 dB | 12 |
| -46 dB | 13 |
| -42 dB | 14 |
| -38 dB | 15 |
| -34 dB | 16 |
| -30 dB | 17 |
| -24 dB | 18 |
| -18 dB | 19 |
| -12 dB | 20 |
| -6 dB | 21 |
| -0 dB | 22 |
| + Infinity | 23 |

### otherPhase

| SAP | MIDI |
| --- | --- |
| In Phase | 0 |
| Out Of Phase | 1 |

### panDepth

| SAP | MIDI |
| --- | --- |
| 1 | 0 |
| x (x=1 to 30 by 1) | x-1 |
| 30 | 29 |
| x (x= 30 to 90 by 3) | (x-30)/3+29 |
| 90 | 49 |
| 100 | 50 |

### pchCents

| SAP | MIDI |
| --- | --- |
| -100 Cents | 0 |
| x Cents (x=-100 to 100 by 1) | x+100 |
| 0 Cents | 100 |
| 100 Cents | 200 |

### pchPitch

| SAP | MIDI |
| --- | --- |
| -24Tones | 0 |
| xTones (x=-24 to 24 by 1) | x+24 |
| 0Tones | 24 |
| 24Tones | 48 |

### pchTrack

| SAP | MIDI |
| --- | --- |
| 0-100 Cents | 0 |
| 0-2 Tones | 1 |
| 1-3 Tones | 2 |
| 1-4 Tones | 3 |
| 2-4 Tones | 4 |
| 3-6 Tones | 5 |
| 4-8 Tones | 6 |
| 6-10 Tones | 7 |
| 8-12 Tones | 8 |
| 12-24 Tones | 9 |

### pchWhammyFunction

| SAP | MIDI |
| --- | --- |
| Shallow Detune | 0 |
| Deep Detune | 1 |
| 1 Octave Above | 2 |
| 2 OctavesAbove | 3 |
| 2nd Below | 4 |
| 1 Octave Below | 5 |
| 2 OctavesBelow | 6 |
| 2ndAbv-3rdAbv | 7 |
| min3Ab-maj3Ab | 8 |
| 3rdAbv-4thAbv | 9 |
| 4thAbv-5thAbv | 10 |
| 5thAbv-6thAbv | 11 |
| 5thAbv-7thAbv | 12 |
| 4thBlw-3rdBlw | 13 |
| 5thBlw-4thBlw | 14 |
| 12Below-12Abv | 15 |

### pchWhammy2Function

| SAP | MIDI |
| --- | --- |
| Deep Detune | 0 |
| 1 Octave Up | 1 |
| Up 2 Octaves | 2 |
| Down 2nd | 3 |
| Down 1 Octave | 4 |
| Down2 Octaves | 5 |
| Down6 Octaves | 6 |
| Up2nd-Up3rd | 7 |
| Upfl3rd-Up3rd | 8 |
| Up3rd-Up4th | 9 |
| Up4th-Up5th | 10 |
| Up5th-Up6th | 11 |
| Up5th-Up7th | 12 |
| Dn4th-Dn3rd | 13 |
| Dn5th-Dn4th | 14 |
| Dn12-Up12 | 15 |

### regenFdback

| SAP | MIDI |
| --- | --- |
| -99 % | 0 |
| x % (x=-99 to -1 by 1) | x+99 |
| Off | 99 |
| x % (x=1 to 99 by 1) | x+99 |
| 99 % | 198 |

### rvbAccentDelay

| SAP | MIDI |
| --- | --- |
| -50ms | 0 |
| xms (x=-50 to 50 by 1) | x+50 |
| 0ms | 50 |
| 50ms | 100 |

### rvbGatedDecay

| SAP | MIDI |
| --- | --- |
| 20ms | 0 |
| xms (x=20 to 100 by 20) | (x-20)/20 |
| 100ms | 4 |
| xms (x=100 to 200 by 25) | (x-100)/25+4 |
| 200ms | 8 |
| 250ms | 9 |
| 300ms | 10 |
| xms (x=300 to 1000 by 100) | (x-300 /100+10 |
| 1000ms | 17 |

### rvbGatedEnvelope

| SAP | MIDI |
| --- | --- |
| Decaying | 0 |
| Flat | 1 |
| Reverse | 2 |

### rvbRT( RvbSize )

| SAP | MIDI |
| --- | --- |
| 1 y Sec (y=0.01*RvbSize) | 0 |
| x y Sec (x=1 to 10 by 1, y= RvbSize*0.01*x) | x-1 |
| 10 y Sec (y=0.10*RvbSize) | 9 |
| x y Sec (x=10 to 15 by 1, y= RvbSize*(0.02*(x-10)+0.10)) | x-1 |
| 15 y Sec (y=0.20*RvbSize) | 14 |
| x y Sec (x=15 to 21 by 1, y= RvbSize*(0.05*(x-15)+0.20)) | x-1 |
| 21 y Sec (y=0.50*RvbSize) | 20 |
| x y Sec (x=21 to 26 by 1, y= RvbSize*(0.10*(x-21)+0.50)) | x-1 |
| 26 y Sec (y=1.00*RvbSize) | 25 |
| x y Sec (x=26 to 30 by 1, y= RvbSize*(0.25* (x-26)+1.00)) | x-1 |
| 30 y Sec (x=2.00*RvbSize) | 29 |

### rvbSpread1

| SAP | MIDI |
| --- | --- |
| 10ms | 0 |
| xms (x=10 to 100 by 10) | (x-10)/10 |
| 100ms | 9 |

### rvbSpread2

| SAP | MIDI |
| --- | --- |
| 25ms | 0 |
| xms (x=25 to 200 by 25) | (x-25)/25 |
| 200ms | 7 |
| 250ms | 8 |
| 300ms | 9 |

### rvbSpread3

| SAP | MIDI |
| --- | --- |
| 20ms | 0 |
| 30ms | 1 |
| 40ms | 2 |
| xms (x=40 to 180 by 20) | (x-40)/20+2 |
| 180ms | 9 |

### smplLooping

| SAP | MIDI |
| --- | --- |
| Manual | 0 |
| Auto | 1 |

### smplManualTrig

| SAP | MIDI |
| --- | --- |
| ( Trigger | 0 |

### smplRecordPlay

| SAP | MIDI |
| --- | --- |
| Record | 0 |
| Playback | 1 |

### smplStartPoint( SmplStopPoint )

| SAP | MIDI - 2 words 1st = 100’s 2nd = 10’s/1’s |
| --- | --- |
| 0.000 | 0 = 0, 0 |
| x (x=0.000 to SmplStopPoint-0.001 by 0.001) | x/0.1, x/0.001 mod 100 |
| 1.499 (SmplStopPoint=1.500) | 1499 = 14, 99 |

### smplStopPoint( SmplStartPoint )

| SAP | MIDI - 2 words 1st = 100’s 2nd = 10’s/1’s |
| --- | --- |
| 0.001 (SmplStartPoint=0.000) | 1 = 0, 1 |
| x=SmplStartPoint+0.001 to 1.500 by 0.001 | x/0.1, x/0.001 mod 100 |
| 1.500 | 1500 = 15, 00 |

### smplTriggerMode

| SAP | MIDI |
| --- | --- |
| Manual Trig | 0 |
| Audio Trg Once | 1 |
| Audio Re-Trig | 2 |

### wetDry

| SAP | MIDI |
| --- | --- |
| All Dry | 0 |
| D99-W01 | 1 |
| Dy-Wx (x=01 to 99 by 1, y=100-x) | x |
| All Wet | 100 |